## Slide 1: HF Radar Skill Assessment
Hugh Roarty
Rutgers University MARACOOS

## Slide 2: Outline
Introduction to HF Radar
Application for Search and Rescue
Assessing Skill of HFR for Search and Rescue
Radial Quality Control

## Slide 3: Introduction to High Frequency Radar
INTRODUCTION TO HF RADAR

## Slide 5: 13 MHz Transmit and Receive Antenna
4 meters

## Slide 7: Standard CODAR Shore Site: Shed, Enclosure, Tx/Rx, Comms, Power, GPS, AIS
Enclosure
Shed
monitor
A.C. unit
transmitter
computer & external hard drive
UPS system
receiver
Two lines of Communication
Lightning Protection

## Slide 8
λ/2
λ/2
λ
λ
Bragg Sea Echo
A
B
C
Freq MHz | λ meters | λ/2 meters | T seconds | C m/s
5 | 60 | 30.0 | 4.4 | 6.7
13 | 23 | 11.5 | 2.7 | 3.6
25 | 12 | 6.0 | 2.0 | 3.0
42 | 7 | 3.6 | 1.5 | 2.3
SeaSonde Principles
SeaSonde Principles
Notes: -The leading RADAR wave crest reflects some energy off of wave slope C
-The second RADAR wave crest passes A (with some energy lost to reflection)
-The second wave crest & the reflected energy of the leading wave crest meet at B
-The energy of the second wave crest reflected at B adds coherently with the reflected
energy of the leading wave crest.

## Slide 9
λ/2
λ/2
λ
λ
Bragg Sea Echo
A
B
C
SeaSonde Principles
SeaSonde Principles
Freq MHz | λ meters | λ/2 meters | T seconds | C m/s
5 | 60 | 30.0 | 4.4 | 6.7
13 | 23 | 11.5 | 2.7 | 3.6
25 | 12 | 6.0 | 2.0 | 3.0
42 | 7 | 3.6 | 1.5 | 2.3
Notes: -The leading RADAR wave crest reflects some energy off of wave slope C
-The second RADAR wave crest passes A (with some energy lost to reflection)
-The second wave crest & the reflected energy of the leading wave crest meet at B
-The energy of the second wave crest reflected at B adds coherently with the reflected
energy of the leading wave crest.

## Slide 10
λ/2
λ/2
λ
λ
Bragg Sea Echo
A
B
C
SeaSonde Principles
SeaSonde Principles
Freq MHz | λ meters | λ/2 meters | T seconds | C m/s
5 | 60 | 30.0 | 4.4 | 6.7
13 | 23 | 11.5 | 2.7 | 3.6
25 | 12 | 6.0 | 2.0 | 3.0
42 | 7 | 3.6 | 1.5 | 2.3
Notes: -The leading RADAR wave crest reflects some energy off of wave slope C
-The second RADAR wave crest passes A (with some energy lost to reflection)
-The second wave crest & the reflected energy of the leading wave crest meet at B
-The energy of the second wave crest reflected at B adds coherently with the reflected
energy of the leading wave crest.

## Slide 11
λ/2
λ/2
λ
λ
Bragg Sea Echo
A
B
C
SeaSonde Principles
SeaSonde Principles
Freq MHz | λ meters | λ/2 meters | T seconds | C m/s
5 | 60 | 30.0 | 4.4 | 6.7
13 | 23 | 11.5 | 2.7 | 3.6
25 | 12 | 6.0 | 2.0 | 3.0
42 | 7 | 3.6 | 1.5 | 2.3
Notes: -The leading RADAR wave crest reflects some energy off of wave slope C
-The second RADAR wave crest passes A (with some energy lost to reflection)
-The second wave crest & the reflected energy of the leading wave crest meet at B
-The energy of the second wave crest reflected at B adds coherently with the reflected
energy of the leading wave crest.

## Slide 12
λ/2
λ/2
λ
λ
Bragg Sea Echo
A
B
C
SeaSonde Principles
SeaSonde Principles
Freq MHz | λ meters | λ/2 meters | T seconds | C m/s
5 | 60 | 30.0 | 4.4 | 6.7
13 | 23 | 11.5 | 2.7 | 3.6
25 | 12 | 6.0 | 2.0 | 3.0
42 | 7 | 3.6 | 1.5 | 2.3
Notes: -The leading RADAR wave crest reflects some energy off of wave slope C
-The second RADAR wave crest passes A (with some energy lost to reflection)
-The second wave crest & the reflected energy of the leading wave crest meet at B
-The energy of the second wave crest reflected at B adds coherently with the reflected
energy of the leading wave crest.

## Slide 13
λ/2
λ/2
λ
λ
Bragg Sea Echo
A
B
C
SeaSonde Principles
SeaSonde Principles
Freq MHz | λ meters | λ/2 meters | T seconds | C m/s
5 | 60 | 30.0 | 4.4 | 6.7
13 | 23 | 11.5 | 2.7 | 3.6
25 | 12 | 6.0 | 2.0 | 3.0
42 | 7 | 3.6 | 1.5 | 2.3
Notes: -The leading RADAR wave crest reflects some energy off of wave slope C
-The second RADAR wave crest passes A (with some energy lost to reflection)
-The second wave crest & the reflected energy of the leading wave crest meet at B
-The energy of the second wave crest reflected at B adds coherently with the reflected
energy of the leading wave crest.

## Slide 14
λ/2
λ/2
λ
λ
Bragg Sea Echo
A
B
C
SeaSonde Principles
SeaSonde Principles
Freq MHz | λ meters | λ/2 meters | T seconds | C m/s
5 | 60 | 30.0 | 4.4 | 6.7
13 | 23 | 11.5 | 2.7 | 3.6
25 | 12 | 6.0 | 2.0 | 3.0
42 | 7 | 3.6 | 1.5 | 2.3
Notes: -The leading RADAR wave crest reflects some energy off of wave slope C
-The second RADAR wave crest passes A (with some energy lost to reflection)
-The second wave crest & the reflected energy of the leading wave crest meet at B
-The energy of the second wave crest reflected at B adds coherently with the reflected
energy of the leading wave crest.

## Slide 15
λ/2
λ/2
λ
λ
Bragg Sea Echo
A
B
C
SeaSonde Principles
SeaSonde Principles
Freq MHz | λ meters | λ/2 meters | T seconds | C m/s
5 | 60 | 30.0 | 4.4 | 6.7
13 | 23 | 11.5 | 2.7 | 3.6
25 | 12 | 6.0 | 2.0 | 3.0
42 | 7 | 3.6 | 1.5 | 2.3
Notes: -The leading RADAR wave crest reflects some energy off of wave slope C
-The second RADAR wave crest passes A (with some energy lost to reflection)
-The second wave crest & the reflected energy of the leading wave crest meet at B
-The energy of the second wave crest reflected at B adds coherently with the reflected
energy of the leading wave crest.

## Slide 17: Radial Surface Currents

## Slide 18: Combine Radial Velocity Measurements

## Slide 19: Total Vector Surface Currents: October 27, 2016 23:00 GMT
Long Branch

## Slide 21
25 MHZ Codar at Breezy Pt.
NOAA Buoy 44025
Significant Wave Height (m)
2006 Wave Comparison

## Slide 22: MARACOOS HF RADAR NETWORK
 | 5 MHz | 13 MHz | 25 MHz
U Mass |  |  | 
WHOI |  |  | 
U Conn |  |  | 
URI |  |  | 
Stevens |  |  | 
Rutgers |  |  | 
Delaware |  |  | 
ODU/CIT |  |  | 
UNC |  |  | 
9 | 17 | 8 | 17
46 Stations in Total

## Slide 23: National HF Radar Network
Coverage for 20 Feb 2015
150 HF Radars Registered
121 HF Radars Reporting

## Slide 24
APPLICATION FOR SEARCH AND RESCUE

## Slide 25
Success Stories – Making a Difference
Optimizing HF Radar for SAR using USCG Surface Drifters

## Slide 26: Search and Rescue - 2004

## Slide 27: SAROPS Test Case - 2008 5000 Virtual Drifters + 1 Real Drifter (Black Line): Search Area After 96 Hours
HyCOM
36,000 km2
HF Radar
12,000 km2
232 km
154 km
123 km
100 km
Notes: HYCOM (Low Conf) 48 hours

## Slide 28
May 4, 2009: After a year of testing, NOAA Announces on
U.S. Department of Commerce Website that
MARACOOS CODAR is Operational in SAROPS
Present Activity:
Bring all
sustained regional-scale HFR networks up to operational status in USCG SAROPS
3 West Coast Regions for
California & Oregon are ready.

## Slide 29
ASSESSING SKILL OF HFR FOR SEARCH AND RESCUE

## Slide 30: National Data Requests from SAROPS December 1, 2011 to March 15, 2014
Ocean
Atmosphere

## Slide 31: Drifter Deployment Locations
Cluster | Longitude | Latitude | 
1 | 70d 42m W | 41d 10m N | 30 m isobath south of Martha's Vineyard
2 | 70d 42m W | 40d 32m N | 70 m isobath south of Martha's Vineyard
3 | 73d 38m W | 39d 53m N | ENE of Barnegat Inlet but south of the Hudson Canyon
Planned deployment date May 10-11, 2016

## Slide 32: Drifter Deployment Locations
# | Buoy Number | Date | Group | Description
1 | 43241 | 5/10/16 | 1 | MVCO 30 m isobath
2 | 43372 | 5/10/16 | 1 | MVCO 30 m isobath
3 | 38824 | 5/10/16 | 2 | MVCO 70 m isobath
4 | 43104 | 5/10/16 | 2 | MVCO 70 m isobath
5 | 43340 | 5/10/16 | 3 | NJ
6 | 43346 | 5/10/16 | 3 | NJ
7 | 43411 | 5/10/16 | 3 | NJ

## Slide 33: Normalized Cumulative Lagrangian Separation Liu and Weisberg (2011)

## Slide 34
4
5.1
3.6
Day 1
Day 2
Day 3
Day | S di | S loi | skill
1 | 4 | 5 | 0.2
2 | 4+3.6 | 5+14 | 0.60
3 | 4+3.6+5.1 | 5+14+24 | 0.70
di
loi

## Slide 36: Drifter 43372 Washed Ashore South Dartmouth, MA

## Slide 38: 5 MHz HF Radar

## Slide 39: 13 MHz HF Radar

## Slide 40: 13 MHz HF Radar with QC

## Slide 41: HYCOM

## Slide 42: Skill Scores

## Slide 43
RADIAL QUALITY CONTROL

## Slide 44: Radial Surface Currents

## Slide 49: Outline
Introduction to HF Radar
Application for Search and Rescue
Assessing Skill of HFR for Search and Rescue
Radial Quality Control

## Slide 50: HF Radar Skill Assessment
THANK YOU