## Slide 1: Evaluation of Environmental Data for Search and Rescue
Hugh Roarty
Scott Glenn
April 15, 2016
Wuhan, China
Art Allen

## Slide 4: Wuhan University
The most beautiful university in China

## Slide 5: Talk Outline
Introduction to MARACOOS
Introduction to High Frequency Radar
Application for Search and Rescue
Evaluating Environmental Data in SAROPS
Global HF Radar Task

## Slide 6: Regional Observing System - MARACOOS

## Slide 7
U..
Cape
Cod
Cape
Hatteras
NJ
MA
CT
VA
DE
NY
NC
RI
MD
PA
10 States - 76 Million People
1000 km Cape to Cape
Middle Atlantic
Regional Association
Coastal
Ocean Observing System
MARACOOS:
A Sustained Real-time Observation & Forecast System
>40 PIs
>20 Institutions
>50 Members
>2000 Contacts
Notes: 7

## Slide 8
MID-ATLANTIC REGIONAL DRIVERS
Ocean Circulation
Tropical Storms
Population
Ports
Northeasters
Climate Change
Critical Habitat

## Slide 9
MARACOOS REGIONAL THEMES
2) Ecosystem Decision Support - Fisheries
4) Coastal Inundation - Flooding
5) Energy – Offshore Wind
1) Maritime Operations – Safety at Sea
3) Water Quality – a) Floatables, b) Hypoxia, c) Nutrients

## Slide 10
To seek, discover & apply new knowledge & understanding
of our coastal ocean
Satellites
HF-Radar
Atmosphere & Ocean Forecast Ensembles
Weather Stations
Population Density
Gliders
Drifters
Notes: Need to cut off cold pool in south and bend offshore
Need to experiment with dulling down the colors in the pop density. Maybe orange/tan to white like the box I put in?
Put gliders just below the lines in 3 of them, and increase their angles facing up and down randomly. I stuck in cheesy examples
I already put the shadow and 80% clear line around the two new maps in the upper right, so we are good there.

## Slide 11: MARACOOS HF RADAR NETWORK
 | 5 MHz | 13 MHz | 25 MHz
U Mass |  |  | 
WHOI |  |  | 
U Conn |  |  | 
URI |  |  | 
Stevens |  |  | 
Rutgers |  |  | 
Delaware |  |  | 
ODU/CIT |  |  | 
UNC |  |  | 
10 | 17 | 8 | 17
42 Stations in Total
10 organizations

## Slide 12: Introduction to High Frequency Radar

## Slide 13: 13 MHz Transmit and Receive Antenna
4 meters

## Slide 14: Surface Current Mapping Capability
25 MHz
Radar l: 12 m Ocean l: 6 m
Range: 30 km Resolution: 1 km
13 MHz
Radar l: 23 m Ocean l: 12 m
Range: 80 km Resolution: 3 km
05 MHz
Radar l: 60m Ocean l: 30 m
Range: 180 km Resolution: 6 km

## Slide 15: Radial Map of Currents

## Slide 16
30 cm/s
20 cm/s
15 cm/s
10 cm/s
5 cm/s
0 cm/s
25 cm/s
April 3, 2016
24 Hour Average
17 Sites
5 MHz
1000 km coastline
6 Km Spatial Resolution

## Slide 17
30 cm/s
20 cm/s
15 cm/s
10 cm/s
5 cm/s
0 cm/s
25 cm/s
7 Sites
13 MHz
200 km coastline
2 Km Spatial Resolution

## Slide 18
30 cm/s
20 cm/s
15 cm/s
10 cm/s
5 cm/s
0 cm/s
25 cm/s
3 Sites
25 MHz
40 km coastline
1 Km Spatial Resolution

## Slide 20: HF Radar Detects Tsunamis
6 km offshore
10 km offshore
14 km offshore
18 km offshore
22 km offshore
Long Beach Island, NJ

## Slide 21
HF Radar Application
Search And Rescue
Dr. Hugh Roarty
Dr. Josh Kohut

## Slide 22: USCG Area of Responsibility

## Slide 23: USCG Drifter Deployments
Most SAR cases occur in the envisioned HF Radar Network footprint
Self Locating Data Marker Buoys (SLDMB)
for Search And Rescue (SAR)
January 2006 – December 2007 (2 years)
National HF Radar Network
Notes: Here are the initial deployment positions for our SLDMBs. From these records we selected only those that exceeded 4 days in length

## Slide 24
Drifter
CODAR
NOAA
Long Range 5 MHz Year 2005

## Slide 25: USCG Current Validation
232 km
154 km
Results of a 1-year blind validation study -
For every real drifter deployed at sea:
5000 Virtual Drifters Deployed in SAROPS
Search Areas compared to real drifters every 12 hours
HYCOM 96 hour Search Area
36,000 km2
123 km
100 km
HF Radar 96 hour Search Area
12,000 km2
Notes: Here are the initial deployment positions for our SLDMBs. From these records we selected only those that exceeded 4 days in length

## Slide 26: Evaluation of Environmental Data

## Slide 27: National Data Requests from SAROPS December 1, 2011 to March 15, 2014
Ocean
Atmosphere

## Slide 28: HF Radar
25 hour mean, March 28, 2016 18:00 UTC
Surface Current Maps
HYCOM

## Slide 29: Normalized Cumulative Lagrangian Separation Liu and Weisberg (2011)

## Slide 30
4
5.1
3.6
Day 1
Day 2
Day 3
Day | S di | S loi | ss
1 | 4 | 5 | 0.2
2 | 4+3.6 | 5+14 | 0.60
3 | 4+3.6+5.1 | 5+14+24 | 0.70
di
loi

## Slide 31: Normalized Cumulative Lagrangian Separation Liu and Weisberg (2011)

## Slide 32
HF Radar
HYCOM

## Slide 33
HYCOM

## Slide 34
HFR

## Slide 36
HF Radar
HYCOM
Separation (km) between actual and modeled trajectory after 48 hours

## Slide 37: Trajectory prediction using HF radar surface currents: Monte Carlo simulations of prediction uncertainties
Journal of Geophysical Research: Oceans Volume 111, Issue C12, C12005, 8 DEC 2006 DOI: 10.1029/2006JC003715 http://onlinelibrary.wiley.com/doi/10.1029/2006JC003715/full#jgrc10405-fig-0008
Notes: (a) Separation between actual and predicted drifter position as a function of time since start of prediction, averaged over all trajectory segments that start within the nominal coverage zone for the BI region. The curves with symbols show the mean separation (dashed line and circles) and the 95th percentile separation (solid line and circles) between the real drifter and the predicted position. The dashed and solid lines show respectively the mean distance and the 95th percentile distance that the real drifter moved over the prediction time. (b) The same statistical measures averaged over all segments that both start and end within the 10% coverage zone.
IF THIS IMAGE HAS BEEN PROVIDED BY OR IS OWNED BY A THIRD PARTY, AS INDICATED IN THE CAPTION LINE, THEN FURTHER PERMISSION MAY BE NEEDED BEFORE ANY FURTHER USE. PLEASE CONTACT WILEY'S PERMISSIONS DEPARTMENT ON PERMISSIONS@WILEY.COM OR USE THE RIGHTSLINK SERVICE BY CLICKING ON THE 'REQUEST PERMISSIONS' LINK ACCOMPANYING THIS ARTICLE. WILEY OR AUTHOR OWNED IMAGES MAY BE USED FOR NON-COMMERCIAL PURPOSES, SUBJECT TO PROPER CITATION OF THE ARTICLE, AUTHOR, AND PUBLISHER.

## Slide 40: GEO Global hf radar network

## Slide 41: Global High Frequency Radar Network Previous Meetings
England 2012
Norway 2013
Taiwan 2014
Greece 2015

## Slide 42
Fourth Meeting of the Global High Frequency Radar Network
September 22-23, 2015
Heraklion, Crete, Greece

## Slide 44
U.S. Department of State, Washington DC
July 31, 2003
GEO, the Group on Earth Observations
An Intergovernmental group with 99 Members and 87 Participating Organizations

## Slide 45
Australia, China, Japan, Korea, Philippines and Taiwan are members of GEO
Notes: GEO is a global partnership of governments and organizations that seeks to realize its Vision of “a future wherein decisions and actions for the benefit of humankind are informed by coordinated, comprehensive and sustained Earth observations.” In support of this Vision, through collective voluntary action, the GEO community is implementing a Global Earth Observation System of Systems (GEOSS) from among a great many individual Earth observation, information and processing systems.
The Global Earth Observation System of Systems 10-Year Implementation Plan, GEO, 2005, p. 5.

## Slide 46: GEO Objectives
Improve and Coordinate Observation Systems
Advance Broad Open Data Policies/Practices
Foster Increased Use of EO Data and Information
Build Capacity

## Slide 47: Goals for Global HF Radar Network
Increase the number of coastal radars
Ensure HFR data is available in a single standardized format in near-real-time,
Assimilate data into ocean and ecosystem models
A set of easy to use standard products
Worldwide Quality Standards
Develop emerging uses of HF radar

## Slide 48: Role of Global Network
ROW

## Slide 49: GEO HF Radar Portal

## Slide 50: Global HF Radar Viewer

## Slide 51: ~350 Radars World Wide
Region | Number | Percentage
Americas | 162 | 47%
Europe | 54 | 16%
Middle East | 7 | 2%
Asia | 122 | 35%

## Slide 52: ORCA Meeting Inventory

## Slide 53: Global Inventory
349
381
Philippines
Morocco

## Slide 54: Application Success Stories

## Slide 55: Talk Outline
Introduction to MARACOOS
Introduction to High Frequency Radar
Application for Search and Rescue
Evaluating Environmental Data in SAROPS
Global HF Radar Task

## Slide 56
THANK YOU
Evaluation of Environmental Data for Search and Rescue