## Slide 1
Gliders: a maturing technology To Study
Ecosystem Dynamics in the Ocean
Rutgers Center of Ocean Observing Leadership:
Oscar Schofield, Josh Kohut, Travis Miles, Grace Saba
Teledyne Webb: Clayton Jones, Doug Webb

## Slide 2
Fundamental challenge for understanding marine ecosystems is to collect sustained spatial relevant physical, chemical, and biological data to increase fundamental knowledge

## Slide 3
Glider’s are buoyancy driven “steerable” underwater vehicles with real-time communications, developed by multiple groups funded by ONR
Buoyancy pump in  the glider pulls in 0.5 L of water
Glider begins to dive downward
Push pump out  glider inflects and begins to climb to the surface
one dive and one climb is called a ‘yo’
When surfacing to connect glider inflates air bladder
Iridium Antenna
ARGOS and
FreeWave Antennas
At programmed
intervals

## Slide 4
Glider’s are “steerable” underwater vehicle with real-time communications that can cover great distances over long periods
-Long duration
-Grand space scales
Moline et al. 2009

## Slide 5
These systems can now collect data over scales similar to remote sensing technologies
SST
Chl
Chl

## Slide 6
Glider history and our timeline of their evolution
Time
1989 (Stommel’s
Sloccum Mission)
1999 (Test Flight)
2003 (First cross
shelf mission)
2009 (First
Basin Crossing)
Glider history
2011-2012
(Hurricane missions)
2013-2014 (South
Atlantic gyre w/
Challenger)
Doug with first at sea test
2006 (First
Antarctic mission)

## Slide 7
Gliders are being accepted by the community and
are having science impact
Publications that used glider data
Year
Glider Design
& Description
Glider Networks
& Observatories
Water Column
Physics
Ocean
Circulation
Plankton
Ecology
Biogeochemistry
Fish
& Birds
Climate
Education
Engineering & Planning (28%)
Physical Oceanography (35%)
Biology and Chemical Oceanography (32%)
Schofield et al. MTS 2015

## Slide 8
What can science data can be collected by gliders?
Schofield et al. MTS 2015
Macro/ Micro
nutrients & chem
Chl a
Proteins
Lipids
Carbos
TEP, DOM
e-
Marine snow & Export Flux
Concentration
Spectral Backscatter
Hyperspectral Absorption
Chlorophyll fluorescence
Imagery (visual, holography)
Diversity
Spectral Backscatter (proxy for composition/size)
Imagery (visual, holography)
“Omics”
Rates
Kinetic fluorescence
Photoacoustics
Stimulated oxygen kinetics
Phytoplankton
Organic Matter Flux
Concentration
Spectral Backscatter spikes
Particle settling rate
Imagery (visual, holography)
Diversity
Imagery (visual, holography)
“Omics”
Mass Spectrometers
Rates
Spatial calibrated fall rates
via imagery
Zooplankton
Concentration
Acoustic backscatter
Imagery (visual, holography)
Diversity
Multi frequency Acoustics Imagery (visual, holography)
“Omics”
IN SITU
OPTICS
Inherent optics
Absorption (l)
Scattering (l)
Volume scattering
Attenuation (l)
Refractive Index
Apparent Optics
(l) Light intensity
up & down
Concentration
Acoustic backscatter
Imagery (visual, holography)
Passive acoustics
Acoustic tags + Receiver
Diversity
Multi frequency Acoustics Imagery (visual, holography)
“Omics”
Passive acoustics
Acoustic tags + Receiver
Higher Trophic Levels
Optical Oxygen
Optical CO2
Mass Spectrometers
TRACE GASES
Optical nutrients
Optical CO2
Optical pH
Mass Spectrometers
CHEMISTRY
TRANSPORT
ADCP
Estimated geostrophic
currents
WATER
COLUMN
PHYSICS
Temperature
Salinity
Turbulence

## Slide 9
Phytoplankton communities
Phytoplankton biomass
Phytoplankton response
To passage of Nor’Easter
storm
Gliders can provide high resolution biomass and taxa estimates

## Slide 10
%Mineral (in situ)
salinity
bb650
cb650
Cb650/bb650
Empirical algorithms
Glider’s provide insight into the nature of phytoplankton composition

## Slide 11
Towed MCM detection system
MIREM April 2005
Clear water
Real water
April 26, 2005
Clear water
Real water
April 24, 2005
probability of detection
at an altitude of 10m
off bottom
Red = poor detection
An example for a very applied problem: What can you see?
Helicopter or diver….
From the optics, one can calculate water column turbidity. What is the depth of the euphotic zone?

## Slide 12
Biomass Proxy (Fm)
Quantum Yield of Photosynthesis (Fv/Fm)
Daytime
Night
Night
Daytime
Night
Night
0
50
25
0
50
25
02/20
02/21
Time (month/day)
02/20
02/21
Time (month/day)
0
0.6
0.3
0
8000
4000
The ability to look at phytoplankton physiology and rate processes
PROXY FOR BIOMASS
HEALTH

## Slide 13
State of New Jersey is now using gliders to map summer water quality. Is low bottom water oxygen due to outflows from the New York city or is a naturally driven by natural dynamics.
State sponsored state wide surveys providing 3-4 missions each summer, and provides close to 10,000 profiles/summer as opposed to ~150 profiles/summer by ship/
New York
city outflow
Upwelling driven
phytoplankton bloom
Ability to link phytoplankton to watercolumn biogeochemistry

## Slide 14
Autonomous Platforms:
Dissolved Oxygen
2011-2012
Dissolved Oxygen (mg/L)
Temperature (°C)
Ability to link phytoplankton to watercolumn biogeochemistry

## Slide 15
Glider’s provide high resolution maps to link to physical drivers
Mixed layer dynamics determine the presence or absence of phytoplankton blooms

## Slide 16
Active acoustics to map zooplankton community and concentration
Powell & Ohman. 2012
Careful calibration of zooplankton with glider-class ADCP.
Powell & Ohman 2015
Glider resolved to the vertical migration at frontal regions along California.

## Slide 17
Active acoustics to map macro-zooplankton community and concentration
Guihen et al. 2014

## Slide 18
wind speed (m s-1)
Ophelia
Sensor damage?
Saturation?
Animal dynamics via active optics

## Slide 19
Receiver Integrated Glider
Enables coupling of data sets
  Telemetry data
  Temperature
  Salinity
  Productivity
Moves us beyond fixed arrays
Gliders being able to track animals based on passive acoustics

## Slide 20
Building distributed glider communities through Gliderpalooza
IOOS (<10% gliders), NASA, Navy, NERC, OOI, EPA, SECOORA, Teledyne, ONR, VIMS, GLERL, CONCORDE
2013
2014

## Slide 21
Gliders being able to track animals based on passive acoustics
Drs. Baumgartner (WHOI) and Fratantoni (SeaTrec) from to develop autonomous gliders, equipped with a reliable acoustic detection algorithm to allow near real time detection of North Atlantic right, fin, sei and humpback whales.
Dr. Baumgartner
Dr. Fratantoni

## Slide 22
Coming soon (2-4 years) micro- and small zooplankton imaging
Holographic images from Monterey
by an AUV
Thanks to James Bellingham (WHOI)
Design strategies are underway

## Slide 23
A)
Antarctic Circumpolar Current
2
-2
°C
0
600
Depth (m)
Gliders assessing biological hotspots
Depth (m)
120
0
0
>1
<-1
Temperature (C)
-64.8
-64.9
-64.3
-63.9
Longitude
Latitude
0
>1
<-1
Temperature (C)
Depth (m)
0
120
-69.4
-68.4
Longitude
-67.7
Latitude
-67.9
Rothera

## Slide 24
Penguin
Foraging
locations
Kahl et al., 2010
Dynamic analysis of penguin foraging in the vertical

## Slide 25
Dynamic analysis of penguin foraging in space

## Slide 26
=
Use thermal niche model + temperature hindcasts ~ estimate habitat distribution in NW Atlantic
Glider data improving model simulations opening the door to ecosystem trajectories
Glider
temperature
Glider
salinity
ROMs
temperature
ROMs
salinity

## Slide 27
Glider data provides direct data into undergraduate class to improve STEM education

## Slide 28
NOAA glider tools provides direct data into undergraduate class to improve STEM education

## Slide 29: Observed Model vs Glider Differences (Results from undergrad summer research)
Most variation between the two models and RU29 exist within the first 300 meters of the water column
MyOcean model has a fairly consistent 1˚C to 2˚C difference in temperature from RU29
RTOFS model was fairly consistent with the RU29 data at lower depths but had very large discrepancies in magnitude at certain locations.
New tools open data analysis across demographic, opportunities for unique crowd sourcing opportunities

## Slide 30
Hurdles: Substrates for formation of artificial reefs
NSF OOI Glider Argentinean Basin
Hurdles: Biofouling (see below), pace of sensor integration, slow but accelerating rate of standardization (Calibration, Qa/Qc, etc)

## Slide 31
40
31
22
13
4
http://rucool.marine.rutgers.edu
Thank You!