## Slide 1: OOI Data Management and QA/QC: Lessons Learned and the Path Ahead
Michael F Vardaro, M. Crowley, L. Belabbassi, M. Smith, L. Garzio, F. Knuth, J. Kerfoot, S. Glenn, O. Schofield, S. Lichtenwalner
Rutgers University, Dept. of Marine & Coastal Sciences, New Brunswick, NJ

## Slide 2: Table of Contents:
OOI Data Evaluation Team
OOI Data Flow
OOI Data Evaluation Procedures
Lessons Learned
  Metadata
  Communications
  QA vs. QC
Future Plans

## Slide 3
OOI By the Numbers
Arrays
Stable Platforms
Moorings, Profilers, Nodes
Mobile Assets
Gliders, AUVs
Instruments
Science Data Products
Science/Engineering Data Products
7
50
33
>850
>2500
>100K

## Slide 4
OOI Operations:
12 FTEs
OOI Management: Steady State: 1 FTE
Rutgers Support
Software Team Manager
Bill Kish
Data Evaluator
Friedrich Knuth
CI PI
Manish Parashar
Program Management
Data Manager
Mike Vardaro
Science PM
RU – Mike Crowley
Science/User PI
Scott Glenn
Leadership
&
Oversight
Software Configuration & Maintenance
Janeen Pisciotta
Data Team
Data Evaluator
Mike Smith
Software Team
Asst. Data Manager Leila Belabbassi
Data Evaluator
Lori Garzio
IT Manager
Juan José Villalobos
System Team
Technical Help Desk & Education-Outreach
Sage Lichtenwalner
User Services Team
System Engineering PM
RU – Ivan Rodero
Project Coordinator
Caroline McHugh
Science/User PI
Oscar Schofield
System Administrator
Aamir Jadoon
Software Test Eng.
Matthew Danku
Network Engineer
Jim Housell
RDI2
COOL
Data Team

## Slide 5: Data Flow

## Slide 6: OOI Data Product Levels
Raw data: The datasets as they are received from the instrument
  May contain multiple L0, L1, or L2 parameters, data for multiple sensors, and be in native sensor units
  Always persisted and archived by the OOI
  Example: format 0 binary file from an SBE-37IM on a Global Flanking Mooring.
Level 0 (L0): Unprocessed, parsed data parameter that is in instrument/sensor units and resolution
  Sensor by sensor (unpacked and/or de-interleaved) and available in OOI supported formats (e.g., NetCDF)
  Always persisted and archived by the OOI
  Example: SBE-37IM Temperature portion of the hex string
Level 1 (L1): Data parameter that has been calibrated and is in scientific units
  QC may be applied at this level, utilizing simple automated techniques or human inspection
  Actions to transform Level 0 to Level 1 data are captured and presented in the metadata of the Level 1 data
  Example: SBE-37IM Temperature converted from hex to binary and scaled to produce degrees C
Level 2 (L2): Derived data parameter created via an algorithm that draws on multiple L1 data products
  Products may come from the same or from separate instruments
  Example: SBE-37IM Density and Salinity

## Slide 7: Data Flow Example: Pioneer Profiler
Instrument
Profiler Controller
Inductive Modem
Platform Controller
Telemetry
OMC Platform Shore Server
OMC Data Server
RU Acquisition Point Server
Dataset Agent
Driver
uFrame Database
Data Product Algorithm
GUI
User
Inductive Modem
CTDPF
DOFST
FLORT
PARAD
VEL3D
MOPAK RTE
Iridium
rsync
Data Files from CGSN
Ocean
WHOI
Rutgers
ADCPS/T

## Slide 8: Data Processing Flow
Acquisition Point Server
(RU)
Dataset Agent
Driver
(Omaha)
uFrame Database
(Omaha)
Data Product Algorithms, QC, A/A
(Omaha)
GUI
(ASA-RPS)
Data files
from CGSN (Telemetered and Recovered)
Cal Sheets
(MIOs)
Preload
Database
(All)
QC Parameters
(RU)
Ingestion Sheet (.csv)
(MIOs/RU)
Cabled Ingest Config
(MIOs/SD)
Algorithms
(OSU)
A/A
Parameters
(MIOs)
Data from RSN
Recorded
Streaming
User

## Slide 9: Data Access Points
Data Portal (GUI)
THREDDS Server
  Aggregated data products in NetCDF and CSV
  ERDDAP (Spring-Summer 2016)
Raw data files (Spring 2016)
Shipboard Data
Large Format Data
  Still Camera & HD Video
  Seismic Sensors
  Hydrophones
  Bioacoustic Sonar
Direct Pass to community organizations (e.g. seismic to IRIS)

## Slide 10: OOI Essential Ocean Variables (EOVs)
All Arrays, all platforms:
  CTD data products (Temperature, Conductivity, Pressure, Density, Salinity)
  Dissolved Oxygen
  ADCP (all series)
  Bulk Meteorology (all products)
  Surface Wave Spectra – significant wave height
  Fluorometric Products (CDOM/Chlorophyll/Backscatter)
  Nitrate
  Seawater pH
  In-Water and Air/Sea pCO2
Cabled Array EOVs (these instruments are only on the Cabled Array):
  HD Camera Products
  Bottom Pressure/Tilt Products
  Seafloor Pressure
  Low-Frequency Hydrophone Products
  Vent Fluid and Particulate DNA Sampler – D1000 Temperature Products

## Slide 11: QC Procedures and Tools

## Slide 12: Data Evaluation Team QA/QC Testing

## Slide 13: OOI Automated QC Procedures
7 automated QC algorithms can produce 8 flags (including logical “or” which combines flags) which are plottable and are included in downloaded files
Coded based on specifications written by OOI Project Scientists, derived from QARTOD manuals and other observatory experiences
Algorithms refer to “lookup tables” assembled by OOI Project Scientists with input from subject matter experts: https://github.com/ooi-integration/qc-lookup
Global Range Test
Local Range Test
Spike Test
Stuck Value Test
Trend Test
Temporal Gradient Test
Spatial Gradient Test (Profile)

## Slide 14: QC Challenges
Local range values will require ongoing gathering of environmental data for each platform
Spike test is currently very simple, and needs tweaking to avoid false positives/negatives (especially in biological data) and to work with certain data types
Trend test may not work as designed, because it requires the system to compare data prior to the user request date
Gradient test is complicated to apply, requires 2D dataset
Not all QC algorithms apply to all data products – ongoing review with Project Scientists
The QC algorithms do NOT trigger alerts in the system
  Alerts/alarms only trigger when new data is telemetered/streamed
  Can set alerts on L1/L2 data streams based on Global/Local range values

## Slide 15: Data Evaluation Procedures & Tools
Data Management Plan (Spring 2016):
  1102-00000_Data_Management_Plan_OOI
Data QA/QC and Sampling Plan:
  1102-00300_QAQC_Cal_Physical_Samples_OOI
Sampling Strategy Document:
  1102-00200_Observation_and_Sampling_Approach_OOI
Data Product Specifications:
  1341-000xx (DPS) and 1342-000xx (Data Flow)
Data Product and QC Algorithms:
  github.com/ooici/ion-functions/tree/master/ion_functions/data
  github.com/ooici/ion-functions/tree/master/ion_functions/qc
Quality Control Lookup tables:
  github.com/ooi-integration/qc-lookup
Data Team download and plotting tools:
  github.com/najascutellatus/plot-nc-ooi

## Slide 16: Lessons Learned

## Slide 17: Metadata standards
Process of defining, collecting, and determining presentation of metadata has been ongoing for longer than anticipated
Software developers interpreted metadata standards differently than intended by the science requirements
Climate and Forecast (CF-1.6) standards adopted
Presentation in NetCDF header is incomplete but being improved
Provenance contained within file, which is not standard
  Encoded in JSON format, requires extraction
  Contains error notifications and information on how product was created
More formatting work needs to be done

## Slide 18: Communication
The main method of communication from the data team to users is via annotation (requires enhancement)
Main method of communication from users to data team is through help desk requests (via website)
Also needed to standardize and improve communication between data team and Marine Implementing Organization personnel

## Slide 19: QA vs. QC
Quality Control is a product check to identify flaws or defects
Quality Assurance is a defined process used to diagnose why a product is flawed or being produced incorrectly
The data team has had to become increasingly familiar with the end-to-end production of data products
Wider teamwork required to track (sometimes mysterious) issues back to a specific cause
  Software error or missing data vs…
  Instrument miscalibration by vendor vs…
  Instrument settings changed during deployment vs…
  Mooring run over by ship

## Slide 20: Future Plans

## Slide 21: Near-Term Priorities
Deliver high quality data to the community, enabled and accelerated via feedback and community “eyes” on the products
  Requires transparency in software releases, QC procedures, and documentation
Hybrid data delivery approaches to augment asynchronous data delivery via GUI, using THREDDS, ERDDAP, etc.
Organize a cross-project team to define and develop a method for post-recovery secondary calibration. This group will rely on external community input.
Several high value and high interest OOI datasets (e.g. bioacoustics, covariance flux measurements, vent fluid chemistry) will require entraining the external community in data quality and delivery discussions
Addition of a data forum and additional communications to external scientists
  OOI is more then a collection of sensors: an ongoing distributed community discussion

## Slide 22: OOI at Oceans 2016
TOWN HALL TOMORROW AT 12:30pm - Rooms 220-221
Consortium for Ocean Leadership & OOI Booth 611 in Exhibitor Hall
Posters Today at 4pm
  OD14A-2394 - OOI Data Access and Visualization via the Graphical User Interface - Lori Garzio
  OD14A-2397 - The Ocean Observatories Initiative: Unprecedented access to real-time data streaming from the Cabled Array through OOI Cyberinfrastructure - Friedrich Knuth
  OD14A-2396 - OOI Data Acquisition Functions and Automated Python Modules - Mike Smith
  OD14A-2399 – OOI Data Pre-Processing: Diagnostic Tools to Prepare Data for QA/QC Processing - Leila Belabbassi
Poster Thursday 4pm
  ED44B-1728: The OOI Ocean Education Portal: Enabling the Development of Online Data Investigations - Sage Lichtenwalner

## Slide 23: Questions?
OOI Main Web site: http://oceanobservatories.org
Data Portal: http://ooinet.oceanobservatories.org
Mike Vardaro, Data Manager, OOI CI Data Team
vardaro@marine.rutgers.edu
Acknowledgements: NSF, COL, Rutgers University, University of Washington, WHOI, Oregon State University, RPS-ASA, Raytheon, UCSD/SIO