## Slide 1
CODAR Network
Glider Fleet
L-Band & X-Band Satellite Receivers
3-D Nowcasts
& Forecasts
Rutgers University - Coastal Ocean Observation Lab
Observatory Operations, Data Fusion & Training Center
Notes: 1

## Slide 2
Regional Priority Themes | Regional Observation & Modeling Capabilities |  |  |  |  | 
 | Weather Mesonet | HF Radar Network | Statistical STPS | Satellite Imagery | Glider Surveys | Dynamical Ocean Forecasts
Theme 1. Maritime Commerce & Safety | Operational Input to USCG SAROPS | Operational input to USCG SAROPS | Operational input to USCG SAROPS | SST for survivability planning | Assimilation dataset for forecast models | Surface currents for SAROPS
Theme 2. Fisheries | Weather forecast ensemble validation | Circulation and divergence maps for habitat |  | SST & Color for habitat | Subsurface T & S for habitat | 3-D fields of T, S, circulation for habitat
Theme 3. Public Health & Water Quality | Winds for transport, river plumes, & upwelling | Surface currents for floatables, bacteria, spill response | Surface currents for floatables, bacteria, spill response | Ocean color for river plumes | Nearshore dissolved oxygen surveys | Surface currents for floatables, bacteria, spill response
Theme 4. Coastal Flooding | Weather forecast ensemble validation | Assimilation dataset for forecast models |  | SSTs assimilation into forecast models | Assimilation dataset for forecast models | Nested forecast ensembles
Theme 5. Offshore Energy | Historical analysis & wind model validation | Historical current analysis & wind model validation |  | Historical analysis surface fronts & plumes for siting | Historical analysis of subsurface fronts & plumes | Coupled ocean-atmosphere models for resource estimates
Integration Matrix: Capabilities Support Multiple Themes
MARACOOS Integration Matrix

## Slide 3
 | Bays, Rivers, Near Shore (< 3 NM) | Offshore (> 3 NM to 200 NM) | Total
Cases | 2,433 | 247 | 2,688
Lives Saved | 500 | 96 | 596
Lives Assisted | 3,332 | 319 | 3,651
Lives Lost | 160 | 14 | 174
Search And Rescue Cases
in MARACOOS Region
U.S. Coast Guard Search And Rescue Data, FY2014

## Slide 4
4 meters
CODAR Omnidirectional
Direction Finding (DF)
13 MHz Combined
Transmit and Receive Antenna

## Slide 5: Resilient CODAR Shore Site: Shed, Enclosure, Tx/Rx, Comms, Power, GPS, AIS
Enclosure
Shed
monitor
A.C. unit
transmitter
computer & external hard drive
UPS system
receiver
Two lines of Communication
Lightning Protection

## Slide 6: Surface Current Mapping Capability
25 MHz
Radar l: 12 m Ocean l: 6 m
Range: >30 km Resolution: 1 km
13 MHz
Radar l: 23 m Ocean l: 12 m
Range: >80 km Resolution: 3 km
05 MHz
Radar l: 60m Ocean l: 30 m
Range: >180 km Resolution: 6 km

## Slide 7
Mid-Atlantic Bight HF Radar Network
Mid-Atlantic HF Radar Network
17 Long-Range CODARs
8 Medium-Range CODARs
16 Short-Range CODARs
41 Total CODARs in Region
+5 CODARs Roaming
46 Total CODARs
Triple Nested, Multi-static, Multi-use
Industry Partner: CODAR Ocean Sensors
1000 km
Cape to Cape

## Slide 8
HFR Data Quality Assurance/Quality Control (QA/QC)
Plotting QC flags in real time
From
QARTOD
Manual for
HF Radar
Regional Information Coordination Entity -
RICE

## Slide 9: Generate Surface Current Maps Every Hour for a Decade
5 MHz- 17 Stations
13 MHz- 7 Stations
25 MHz- 16 Stations
Outside- 6 Stations
TOTAL – 46 Stations
Winter Storm Jonas
2016/01/23 20:00 UTC
Decadal Mean Currents
for Spatial Planning
Hourly Maps for
Search And Rescue

## Slide 10: Search And Rescue Data Availability Metrics
MARACOOS 17-Site Long Range Network:
Consistently exceeds U.S. Coast Guard 80-80 Metric
80 % spatial coverage 80% of the time
Achieved through site resiliency and active spares approach.
Accomplished with 2.5 Field Technicians
Every
6 Months since 2011

## Slide 11
Bottom temperature
Data used [… real-time SOURCE] *THREDDS Data Server
72-hour forecast NAM 0Z cycle at 2 am EST [NCEP NOMADS]
RU regional CODAR hourly [RU TDS*]
RU glider T,S [RU TDS]
USGS daily average flow available 11:00 EST [USGS waterdata]
AVHRR IR passes 6-8 per day [MARACOOS TDS]
REMSS MW-IR blended SST daily average [NASA PO-DAAC]
HYCOM NCODA 7-day forecast updated daily [NRL]
Jason-2, CryoSat, AltiKa along-track altimeter OGDR [RADS.nl]
SOOP XBT/CTD, Argo floats, on GTS [NOAA OSMC ERDDAP]
Rutgers ROMS 4DVAR uses all available data from a modern coastal ocean observing system
  more and diverse data is better (T, S, u, sea level)
  bias correction to OBC and MDT is essential
Useful subsurface skill for real-time applications:
  4 days for temperature and salinity;
  1-2 days for velocity
Future directions: variational methods for observing system design; coupling; ecosystems
4-day forecast
2-day forecast
Data assimilation analysis/hindcast
Forward model after bias removal
Forward model
depth
correlation

## Slide 12
Transition Objective –
Operational Use of HF Radar Surface Currents for Search And Rescue
Surface Currents
Search And Rescue Optimal Planning System (SAROPS)
Data Acquisition
Data Product Generation & Management

## Slide 13: 2011-2014 2016-2017
USCG SAROPS Ocean Current Product Requests
Global HYCOM Products – Always there “100-100” metric
HF Radar Data & Statistical Predictions – #8
Assimilative Regional Espresso ROMS - not on the list
Global HYCOM Products – Still Always there “100-100” metric
HF Radar Data & Statistical Predictions – up to #6
Assimilative Regional Espresso ROMS - up to #4

## Slide 14
HFR Data
Navy HYCOM Region 1
2016 Surface Current Drifter Skill Score
National Search and Rescue School
Yorktown, VA
January 19, 2017
Coast Guard Sector NY
Staten Island, NY
March 21, 2017
Active Education & Outreach to USCG Users of the HFR Data & Data Assimilative Products
No HFR Assimilation

## Slide 15: Coast Guard Wind & Current Data Requests
Requests June 1 to December 1, 2017

## Slide 16
Winter Storm Jonas
2016/01/23 20:00 UTC
5 MHz- 17 Stations
13 MHz- 7 Stations
25 MHz- 16 Stations
Outside- 6 Stations
TOTAL – 46 Stations
Nested High Resolution HF Radars in NOAA PORTS

## Slide 17
New Jersey 13 MHz
Medium Range HF Radar Network – Nearshore Waves
HFR wave observations combined with co-located Surfcams
Gap fills a sparse buoy network in regions of high variability & interest

## Slide 18
SEAB
44065
SPRK
44091
BRNT
WOOD
Winds become seaward at the times listed below, shown in time series plots with vertical lines. The first transition occurs at WOOD and progresses northward:
SEAB (19:00)
SPRK (18:00)
44065 (17:00 / 18:00)
BRNT (17:00)
WOOD (14:00)
Significant Wave Height (m) Versus Time
Landward Winds For First Half+ of March 14, 2017

## Slide 19
RC10
RC5
RC3
44091
SPRK
Buoy 44091 , SPRK: RC10 RC5 RC3
Significant Wave Height (m) Versus Time
Seaward Winds: March 22-23, 2017
landward
seaward
Significant wave height data are displayed for RC10, RC5, and RC3 and for buoy 44091.
Seaward winds are reflected in a seaward increase in wave height extending through SPRK range cells and the buoy.

## Slide 20
New Jersey 13 MHz
June 13, 2013 Meteo-tsunami
Medium Range HF Radar Network – Tsunami Detection

## Slide 21
Summary:
Integrated, Sustained and Certified Regional Ocean Observing Systems are operating in the U.S.
Transformational Observing Technologies (HF Radar & Gliders) Key to Success
Integrated approach demonstrates every day that knowledge of the ocean improves weather forecasts
Global Glider & HF Radar networks are forming – participation is welcomed
Indian Ocean Glider/Model Validation Mission ongoing – collaborators are welcomed
Workforce Training is ongoing – students are welcomed – BMKG Academy, Rutgers Masters Operational Oceanography