## Slide 1
U..
Cape
Cod
Cape
Hatteras
Mid-Atlantic Bight (1000 km Cape to Cape)
78 Million People (1/4 of U.S.)
Irene + 10
Sandy
Integrated
Ocean-Atmosphere Observing and Forecasting
Jose
Scott Glenn, Travis Miles,
Oscar Schofield, Grace Saba,
Josh Kohut, Joe Brodie,
Hugh Roarty, Mike Crowley
Cliff Watkins, Greg Seroka
(Rutgers)
+ Many More
Hurricanes
Notes: 1

## Slide 2: U.S. Integrated Oean Observing System (IOOS)
  Global Component
  US contribution to Global Ocean Observing System (GOOS)
  1 of 15 Regional Alliances of GOOS
  National Component
  17 Federal agencies
Regional Component
  11 Regional Associations
    Stakeholder driven
    Academia, state/local/tribal government, private industry
Partnership effort that leverages dispersed national investments to deliver ocean, coastal and Great Lakes data relevant to decision-makers.
Notes: NOAA is the Lead Federal Agency
US IOOS program office is within NOAA, but intended to be a multi agency network and federal to non-federal so we use the term U.S. IOOS.
Additional Background:
US IOOS is a national endeavor and spans from global to coastal, with federal and non-federal partners. The majority of non-federal partners are represented by 11 Regional Associations (RAs) that represent the US EEZ and Great Lakes.

## Slide 3
2000 km
2000 km
Many Nations with Similar Regional, National and International Interests

## Slide 4: GOOS Strategic Mapping
New GOOS
Observing Elements:
1) HF Radar
2) OceanGliders
Notes: This activity will allow us to improve a Strategic Mapping of GOOS, which is shown here linking the three major societal drivers of GOOS: climate, services, and ocean health; with the societal benefits informed by sustained ocean data; the scientific issue, application, or product needed; the Essential Ocean Variable we need to capture; and the type of observing element contributing to the measure of these variables.
We can track how any particular observing platform measures a number of variables, feeding products and applications that deliver societal benefit.
A major message from this complicated diagram is that there are many interconnections. Many observations have multiple lifetimes – multiple uses. With growing sensor capability we are increasingly building an integrated observing system. And there is a tremendous needs for the coordination activities that make this system as efficient and effective as possible.
Behind each of the nodes in this mapping that we continue to build is a specification sheet with additional information on the global groups and standards and best practices information.
Each GOOS Regional Alliance or national effort will have its own variant of this mapping, based on local priorities and capacities.

## Slide 5
Mid-Atlantic Regional Drivers for Society & Economy
Ocean Circulation
Tropical Storms
Population
Ports
Northeasters
Climate Change
Critical Habitat

## Slide 6
46 Site CODAR Network
468 Glider
Deployments
Satellite Receivers
Glider Lab
Ocean
Modeling
Rutgers University - Center for Ocean Observing Leadership
MARACOOS – A regional implementation of an integrated network
Notes: 6
All of this gets combined into our overall operations, research, and educational initiatives in the “COOL Room,” shown here (with a class in the background)
Thanks to many partners

## Slide 7
Mid-Atlantic Bight HF Radar Network
Mid-Atlantic HF Radar Network
17 Long-Range CODARs
8 Medium-Range CODARs
16 Short-Range CODARs
41 Total CODARs in Region
+5 CODARs Roaming
46 Total CODARs
Triple Nested, Multi-static, Multi-use
Industry Partner: CODAR Ocean Sensors
1000 km
Cape to Cape

## Slide 8
Technology Center for Slocum Robotic Underwater Gliders
1989 Science Fiction Article
1999
First Slocum deployed at Sea
2009 First Atlantic Crossing
2018 Navy Fleet grows >150
Notes: Gliders from Teledyne Webb Research
First deployment: off the end of the dock, tied to a rope in case it didn’t come back.
The “Challenger” mission, which was largely student coordinated throughout the crossing
Currently circumnavigating the Indian Ocean
RU COOL now operates a fleet of 32 (33) gliders, making it the largest academic operator in the world

## Slide 9
Glider Sensors
Inside Payload Bay or External

## Slide 10
Regional Priority Themes | Regional Observation & Modeling Capabilities |  |  |  |  | 
 | Weather Mesonet | HF Radar Network | Statistical STPS | Satellite Imagery | Glider Surveys | Dynamical Ocean Forecasts
Theme 1. Maritime Commerce & Safety | Operational Input to USCG SAROPS | Operational input to USCG SAROPS | Operational input to USCG SAROPS | SST for survivability planning | Assimilation dataset for forecast models | Surface currents for SAROPS
Theme 2. Fisheries | Weather forecast ensemble validation | Circulation and divergence maps for habitat |  | SST & Color for habitat | Subsurface T & S for habitat | 3-D fields of T, S, circulation for habitat
Theme 3. Public Health & Water Quality | Winds for transport, river plumes, & upwelling | Surface currents for floatables, bacteria, spill response | Surface currents for floatables, bacteria, spill response | Ocean color for river plumes | Nearshore dissolved oxygen surveys | Surface currents for floatables, bacteria, spill response
Theme 4. Coastal Flooding | Weather forecast ensemble validation | Assimilation dataset for forecast models |  | SSTs assimilation into forecast models | Assimilation dataset for forecast models | Nested forecast ensembles
Theme 5. Offshore Energy | Historical analysis & wind model validation | Historical current analysis & wind model validation |  | Historical analysis surface fronts & plumes for siting | Historical analysis of subsurface fronts & plumes | Coupled ocean-atmosphere models for resource estimates
Integration Matrix: Capabilities Support Multiple Themes
MARACOOS Integration Matrix

## Slide 11
Regional Priority Themes | Regional Observation & Modeling Capabilities |  |  |  |  | 
 | Weather Mesonet | HF Radar Network | Statistical STPS | Satellite Imagery | Glider Surveys | Dynamical Ocean Forecasts
Theme 1. Maritime Commerce & Safety | Operational Input to USCG SAROPS | Operational input to USCG SAROPS | Operational input to USCG SAROPS | SST for survivability planning | Assimilation dataset for forecast models | Surface currents for SAROPS
Theme 2. Fisheries | Weather forecast ensemble validation | Circulation and divergence maps for habitat |  | SST & Color for habitat | Subsurface T & S for habitat | 3-D fields of T, S, circulation for habitat
Theme 3. Public Health & Water Quality | Winds for transport, river plumes, & upwelling | Surface currents for floatables, bacteria, spill response | Surface currents for floatables, bacteria, spill response | Ocean color for river plumes | Nearshore dissolved oxygen surveys | Surface currents for floatables, bacteria, spill response
Theme 4. Coastal Flooding | Weather forecast ensemble validation | Assimilation dataset for forecast models |  | SSTs assimilation into forecast models | Assimilation dataset for forecast models | Nested forecast ensembles
Theme 5. Offshore Energy | Historical analysis & wind model validation | Historical current analysis & wind model validation |  | Historical analysis surface fronts & plumes for siting | Historical analysis of subsurface fronts & plumes | Coupled ocean-atmosphere models for resource estimates
Integration Matrix: Capabilities Support Multiple Themes
MARACOOS Integration Matrix

## Slide 12
Regional Priority Themes | Regional Observation & Modeling Capabilities |  |  |  |  | 
 | Weather Mesonet | HF Radar Network | Statistical STPS | Satellite Imagery | Glider Surveys | Dynamical Ocean Forecasts
Theme 1. Maritime Commerce & Safety | Operational Input to USCG SAROPS | Operational input to USCG SAROPS | Operational input to USCG SAROPS | SST for survivability planning | Assimilation dataset for forecast models | Surface currents for SAROPS
Theme 2. Fisheries | Weather forecast ensemble validation | Circulation and divergence maps for habitat |  | SST & Color for habitat | Subsurface T & S for habitat | 3-D fields of T, S, circulation for habitat
Theme 3. Public Health & Water Quality | Winds for transport, river plumes, & upwelling | Surface currents for floatables, bacteria, spill response | Surface currents for floatables, bacteria, spill response | Ocean color for river plumes | Nearshore dissolved oxygen surveys | Surface currents for floatables, bacteria, spill response
Theme 4. Coastal Flooding | Weather forecast ensemble validation | Assimilation dataset for forecast models |  | SSTs assimilation into forecast models | Assimilation dataset for forecast models | Nested forecast ensembles
Theme 5. Offshore Energy | Historical analysis & wind model validation | Historical current analysis & wind model validation |  | Historical analysis surface fronts & plumes for siting | Historical analysis of subsurface fronts & plumes | Coupled ocean-atmosphere models for resource estimates
Integration Matrix: Capabilities Support Multiple Themes
MARACOOS Integration Matrix

## Slide 13
Hurricane Irene
August 28, 2011
NOAA/NHC Damage:
>$16 Billion.
Track Accurate;
Intensity Over-predicted.
Hurricane Sandy
October 29, 2012
NOAA/NHC Damage:
>$68 Billion.
Track Accurate;
Surge Under-predicted.
Avila & Cangialosi, 2012, Tropical Cyclone Report
Georgas et al., 2014, J. of Extr. Even.
Colle et al., 2015, J. Mar. Sci. & Engr.

## Slide 14
Mid Atlantic
Winter (1-layer)
Mid Atlantic
Summer (2-layers)
Cold Pool
To characterize the Cold Pool, we need ocean observations that are “fit for purpose”
Essential Ocean Feature - Mid-Atlantic’s Cold Pool
An unseen cold bottom layer beneath a warm summer surface layer
Assimilated into Regional
Ocean Models
Satellite SST
Glider Zig-Zags
or Triangles
Bottom Temperature

## Slide 15
WHAT?
Satellite
SST
Post-Irene
Pre-Irene
Difference
WHY?
HF Radar
Currents
WHEN? Glider Temperature
Eye Passage
11C max Cooling
Essential Ocean Processes:
Ahead of eye center – Vertical Shear > Mixing > Cooling

## Slide 16
WRF Atmospheric Forecast Sensitivity Study – >130 tests
Warm Ocean
Boundary Condition
Cold Ocean
Boundary Condition
IMPACT?
>10 knots reduction in peak wind speed
Cat 1 Hurricane
Tropical Storm

## Slide 17
Irene Essential Ocean Process
Hurricane Sandy
October 29, 2012
NOAA/NHC Damage:
>$68 Billion.
Track Accurate;
Surge Under-predicted.
Glenn et al. 2016 Nature Communications
Georgas et al., 2014, J. of Extr. Even.
Colle et al., 2015, J. Mar. Sci. & Engr.
Ahead of eye cooling also observed in:
10 MAB Hurricanes
1 Yellow Sea Typhoon

## Slide 18
Superstorm Sandy: 1 Day Before Landfall

## Slide 19
Superstorm Sandy: 1 Day Before Landfall

## Slide 20
Hurricane Sandy Potential Energy Anomaly
Well-mixed
Stratified
Stratification Factor
Non-dimensional
PEA
PEA
Essential Ocean Process:
Ahead of eye center advection

## Slide 21
Two types of coastal ocean response
to Mid Atlantic hurricanes discovered
The essential ocean feature is
  the Mid Atlantic Cold Pool.
The essential ocean processes are
  (a) ahead-of-eye cooling vs.
  (b) ahead-of-eye advection.
Including these essential ocean features and processes in the ocean component of coupled hurricane forecast models is essential for improving intensity forecasts for landfalling Mid Atlantic hurricanes.
For the 2018 hurricane season –
  Operational HWRF will use GOFS 3.0 + POM
  Experimental HWF will use GOFS 3.1
New Scientific Understanding:
+ Monthly Weather Review (2016)
+ JGR-Oceans (2017)
+ JGR-Oceans (2017)

## Slide 22
Navy Global Ocean Forecast System (GOFS):
Operational GOFS 3.0
OpTest of GOFS 3.1
Two Thermal layers on Shelf
No Cold Pool
Well Defined
Cold Pool
Nearly Isothermal Shelf
Temperature below summer thermocline in 2017

## Slide 23
Project Title: Sustained ocean observations with underwater gliders in support of hurricane intensity forecasts (2019 and 2020)
Storm Glider Picket Lines

## Slide 24
Integrated Ocean-Atmosphere Observation & Forecast systems:
  Provides a structure for shared investments in Society & the Economy
Operations > Research > Engagement > Operations Cycle
  Proven approach for enhancements & growth
Glider picket lines & improved oceans in coupled forecast models
  Improve hurricane and tropical cyclone forecasts - our Noble Goal
  Benefits multiplied through the Integration Matrix