## Slide 1: Development of a Multistatic HF Radar Network
Mike Smith
Scott Glenn
SICOMAR+ HF Radar Summer School
May 26, 2021
Ethan Handel
Josh Kohut
Hugh Roarty
Laura Nazzaro

## Slide 2
Long Range Network
New Jersey 13 MHz
Block Island Sound
Muskeget Channel
5 MHz - 17 Stations
13 MHz - 8 Stations
25 MHz - 16 Stations
TOTAL – 41 Stations
Western Long Island Sound
New York Harbor
Delaware Bay
Chesapeake Bay
MARACOOS High Frequency Radar Network
Key Applications
Search and Rescue
Coastal Hazards
Maritime Safety
Water Quality Forecasting
Winter Storm Jonas
2016/01/23 20:00 UTC
Notes: Sends a radar signal out across the water
About as much energy as a 100w light bulb
3 types of networks with 3 resolutions
The mid range also measure wave height just offshore.

## Slide 3
March 2017
Wave Measurements from HF Radar Stations
10o
190o

## Slide 4: Growth of HF Radar in the US
MARACOOS Stations
IOOS Stations
Rutgers has been operating
HF Radars since 1996
Jun 14 - Aug 15, 1996
May 1999 - May 2000

## Slide 5: Multistatic Introduction

## Slide 6: Terminology - Monostatic
Tx/Rx
Notes: Constant time-delay paths form circles around HFR
Vectors normal to range circle

## Slide 7: Terminology - Bistatic
Tx
Rx
Notes: Constant time-delay paths form ellipses w/ foci @ Tx & Rx sites
Velocity component normal to ellipse

## Slide 8: Terminology - Multistatic
Tx/Rx
Tx
Notes: Operating the radars in monostatic and bistatic mode simultaneously

## Slide 9: Multistatic Modelling
Signal Strength | Monostatic | Multistatic | Change | % Change
0.00 – 0.25 | 38,138 | 109,820 | 71,682 | 188%
0.25 – 0.50 | 46,444 | 28,725 | -17,719 | -38%
0.50 – 1.00 | 41,700 | 34,719 | -6,981 | -17%
1.00 – 2.00 | 40,444 | 33,669 | -6,775 | -17%
2.00 – 3.00 | 24,600 | 24,756 | 156 | 1%
Total | 191,326 | 231,689 | 40,363 | 21%

## Slide 10: Multistatic Modelling
Signal Strength | Monostatic | Multistatic | Change | % Change
0.00 – 0.25 | 38,138 | 109,820 | 71,682 | 188%
0.25 – 0.50 | 46,444 | 28,725 | -17,719 | -38%
0.50 – 1.00 | 41,700 | 34,719 | -6,981 | -17%
1.00 – 2.00 | 40,444 | 33,669 | -6,775 | -17%
2.00 – 3.00 | 24,600 | 24,756 | 156 | 1%
Total | 191,326 | 231,689 | 40,363 | 21%

## Slide 11: Multistatic Operations

## Slide 12: Radar Spectra
Monostatic
Bistatic 01
Bistatic 02
Bistatic 03

## Slide 13: BRLO QC – Sep 3, 2020 06:00

## Slide 14: Previous BRLO Settings
DC Peak - Range Cell 55
First RC To Process - Range Cell 59

## Slide 15: New BRLO Settings
Made changes on 2020-09-25 18:42 UTC
DC Peak - Range Cell 62
First RC To Process - Range Cell 66
DC Peak

## Slide 16: Quality Control Test
Monthly Flag Rate:
February 2018 to April 2021
No data Suspect
Pass Fail
1
2
4
3
Mean velocity within a range cell
1
Median of all range cell means
3
2
95% confidence interval
4
Median +/- 2 SD
Legend

## Slide 17: Multistatic Verification

## Slide 18
MRCH
MRCH
Receive Station
Transmit Station
AMAG
HEMP
MRAM
MRHE

## Slide 19: Comparison Ellipticals with Radials
MRAM vs. AMAG

## Slide 20: Comparison with Radials
MRAM vs. AMAG
Correlation Coefficient
Root Mean Square Error
August 2018
MRCH
AMAG
MRCH
AMAG

## Slide 21: Comparison with Radials
MRAM vs. AMAG
Correlation Coefficient
Root Mean Square Error
January 2021
MRCH
AMAG
MRCH
AMAG

## Slide 22: Comparison with Drifters
Ellipticals
MRAM: N=131, r=.675, RMSE=13.4
MRHE: N=149, r=.654, RMSE=16.3
August 2018
Radials
MRCH: N=150, r=.845, RMSE=8.8
AMAG: N=121, r=.723, RMSE=12.2
HEMP: N=150, r=.781, RMSE=14.8
HOOK: N=147, r=.875, RMSE=10.4
sldmb65141730

## Slide 23: Comparison with Drifters - Ellipticals
MRHE
MRAM

## Slide 24: Comparison with Drifters - Radials
HOOK
AMAG
HEMP
MRCH

## Slide 25: Conclusions
Rutgers HF Radar Network entering its 25th year
MARACOOS HFR Network entering its 14th year
Multistatics have potential to expand coverage and reduce uncertainty
Elliptical comparisons with drifters on par with radials

## Slide 26: Development of a Multistatic HF Radar Network
SICOMAR+ HF Radar Summer School
May 26, 2021
THANK YOU