## Slide 1: MID ATLANTIC BIGHT: COASTAL UPWELLING & THE OFFSHORE WIND ENVIRONMENT
Sarah Murphy
Dr. Travis Miles (Advisor)
Dr. Josh Kohut
Dr. Matt Oliver (external; University of Delaware)

## Slide 2: Mid Atlantic Bight
High population density
Ecologically diverse
Complex ocean dynamics

## Slide 3: Cold pool
8-10 cold water mass below seasonal thermocline
Forms from remnant winter water over the shelf
Central to structuring MAB ecosystem
Source for coastal upwelling
Cite from scemfis

## Slide 4: Offshore wind
NJ : 50% Renewable Energy by 2030
  Offshore Wind 7500MW by 2035
  1 leased area awarded
Challenges:
  Complex political/regulatory climate
  New offshore conditions
  Variable source to supply energy market

## Slide 5: Cold pool & offshore wind

## Slide 6: Coastal Upwelling:
Stratified ocean
Predominately southerly winds
Cold bottom water driven up along the coast

## Slide 7: Importance of Coastal Upwelling
Fisheries:
Offshore Wind:
influence offshore sea breeze fronts
large coastal blooms, hypoxic bottom conditions
decrease coastal SST 2-8
decrease coastal SST 2-8°𝐂
Highly variable in size/duration
Can occur for up to half of the days of the summer
Highly variable in size/duration
Can occur for up to half of the days of the summer
Glenn et al., 2004

## Slide 8: Thesis Overview
Chapter 1:
Chapter 2:
Use of GOES-16 SST for the detection of coastal upwelling
RU-WRF sensitivity analysis to varying SST fields

## Slide 9: GOES-16
  Available as of Nov. 2017
  Resolution: Hourly, 2km
  Challenge: provided Quality Flag removes upwelling
Quality Flag (QF)
Spike Filter (SF)

## Slide 10
Chapter 1
Case study: Summer 2019
1. Prepare GOES data:
Cloud-correcting
Gap-filling
2. Analyze detection of upwelling

## Slide 11: 1. Methods: Spike Filter
Rate of SST change: >1°C/hour
Minimum SST threshold: 12 °C
Comparison to recent SST: >2 SDs moving 7 day per pixel average
Bias correction (up to +.3 °C)

## Slide 12
Applied Spike Filter
RAW GOES
GOES SF

## Slide 14
 | Quality Filter | Spike Filter
RMS: | .713 | .645
CRMS: | .652 | .626
MB: | .275 | -.055
Count: | 741 | 796
Buoy Validation
(Averaged across 3 buoys)
GOES Spike Filter:
Lower RMS, CRMS, MB
Improved count

## Slide 15: 2. Gap filling: DINEOF
DINEOF is an EOF-based method
Fill in missing data from geophysical fields, such as clouds in SST
Has been widely used and cited
Weighting in time and space
Calculates missing data from an optimal number of EOFs obtained by cross-validation
(Alvera-Azcárte et al., 2009).

## Slide 16: Final product
1. Cloud corrected: Spike Filtered
2. Gap-Filled: DINEOF

## Slide 17
2. Comparison to other satellite products:
 | AVHRR | MUR | GOES-16
Satellite | Polar-Orbiting | observations from several instruments and climatology | Geostationary
Spatial Resolution | ~ 5 km | ~ 1 km | .~ 2 km
Temporal Resolution | Twice Daily | Daily | Hourly

## Slide 18
Buoy Validation
(Averaged across 3 buoys)
GOES DINEOF:
Low RMS error
High Count
 | GOES DINEOF | AVHRR | MUR
RMS: | 0.78 | 1.53 | 0.75
CRMS: | 0.75 | 1.45 | 0.67
MB: | -0.18 | -0.48 | 0.31
Count: | 2314 | 131 | 111

## Slide 20
SST difference (offshore SST – inshore SST) at the 4 upwelling centers in the MAB for the summer time period. GOES DINEOF SST (solid lines) and GHRSST MUR SST(dashed lines) are shown. The upwelling threshold is defined as an SST difference in 2°C or greater.
 | GOES DINEOF | MUR
Total Upwelling Days | 33 | 15
Percent of summer upwelling occurred | 30% | 13.5%
Average upwelling SST | 22.5°C | 22.97°C
Minimum upwelling SST | 17.1 °C | 17.88°C
Maximum SST Diff (Off-Inshore) | 3.4 °C | 3.58°C
Average Duration | 6.5 days | 3 days
Max Duration | 17.66 days | 7 days
Average Area Upwelling | 3223 km2 | 3091 km2
Max Extent Area | 5996 km2 | 5799 km2

## Slide 21
The total area of upwelling SST pixels as detected by GOES DINEOF (blue) and MUR (orange) for the upwelling time period.

## Slide 22
Figure 7. Winds speed and direction from buoy 44009 during GOES DINEOF detected upwelling (left) and non-upwelling (right) times for the summer-time period. The winds are shifted 18 hours earlier than the timing of the upwelling events to account for the local lag in Ekman transport.

## Slide 23
Fig. 8. The median upwelling SST averaged per pixel for the detected upwelling days for GOES DINEOF (33 days)

## Slide 24: Key findings
Upwelling may be occurring more persistently, rather than a series of short episodic events
Less than half the number of total upwelling days observed using GOES DINEOF were observed in MUR SST
Clear detection of the timing and duration of upwelling events is important as it provides estimates for ecological and physical responses in the MAB.

## Slide 25: Chapter 2: Sensitivity of RU-WRF winds to SSTs during Coastal Upwelling
SST important for atmospheric temperature conditions and circulation
SST used as the ocean surface boundary condition in atmospheric modeling and forecasting
Development of offshore wind energy, test the sensitivity of wind forecasting to SST fields
Coastal upwelling creates a higher thermal contrast between the warm land and cold ocean and has been shown to influence sea breeze fronts (Franchito et al. 1998; Seroka et al. 2018)

## Slide 26: Offshore Wind
Offshore wind is a variable source of electricity
Balance the supply and demands of the system
Wind power forecasting is used by wind developers and grid system operators so that they can plan the amount of electricity that will be supplied to the grid

## Slide 28: Chapter 2. varying SST in RU-WRF
  Case study: 7/15/19-7/23/19
  3 SSTs used: GFS, AVHRR, GOES
  Forecasted wind speeds in offshore wind lease areas off of NJ
  Determine the impact on wind power production

## Slide 29: RU-WRF ocean surface boundary conditions

## Slide 30: RU-WRF Winds at OCW1

## Slide 31: Wind Power Production
SST input | Total GWh | Capacity Factor
GFS | 1.3023 | 0.4201
AVHRR Coldest-pixel+ SPORT | 1.3786 | 0.437
GOES | 1.2691 | 0.409
The max. difference in energy production: 90,400 kWh
Equivalent to a difference in energy consumption by ~414 households

## Slide 32: Future studies
Investigate over a longer time period- seasonal
Increase temporal resolution of GOES to hourly updating
Validation of SST and wind speeds could be completed with the newly available data from the Atlantic shores buoy for the following summer time period

## Slide 33: Conclusions
Chapter 1. GOES SST is valuable for the detection of coastal upwelling in the MAB
Chapter 2. Varying ocean surface boundary conditions in RU-WRF affects forecasted wind speeds during an upwelling event in the NJ WEA
GOES SST be valuable for improving our understanding of other regional oceanographic and atmospheric processes

## Slide 34: Acknowledgements
Advisor:
  Travis Miles
Committee:
  Josh Kohut, Matt Oliver
Contributors:
  Laura Nazzaro, Joe Brodie, Jaden Dicopoulos
  James Simkins, Matt Shatley
C2R2 cohort, friends at Rutgers, family for support