## Slide 1
The Historic Flight of RU27:
The Scarlet Knight
The First Underwater Robot
to Cross the Atlantic
Scott Glenn
Coastal Ocean Observation Lab
Institute of Marine and Coastal Sciences
School of Environmental and Biological Sciences
Rutgers, The State University of New Jersey
http://rucool.marine.rutgers.edu/

## Slide 2
CHIP
CTD
Fore Hull
Altimeter
Air Bladder
Control Board
Science Payload Bay
Tailfin &
Rudder
Cowling
Aft Hull
Buoyancy Pump
Antenna
(Iridium, Freewave, GPS & Argos)
What is a Robotic Underwater Glider?

## Slide 3
Glider Diving Behavior
Buoyancy Pump pulls water in, Batteries are pushed forward

## Slide 4
Glider Underwater Navigation
Rudder used to steer a compass heading

## Slide 5
Glider Climbing Behavior
Buoyancy Pump pushes water out, Batteries are pulled back

## Slide 6
Glider Flight Path & Communications
Alternating Dives & Climbs, Surfacing to Phone Home

## Slide 7
CODAR Network
Glider Fleet
L-Band & X-Band Satellite Receivers
3-D Nowcasts
& Forecasts
Rutgers University - Coastal Ocean Observation Lab
On-Campus Observatory Research & Education Center
Notes: 7

## Slide 8
Trans-Atlantic Glider Challenge – May 24, 2006 –
UNESCO E.U./U.S. Baltic Sea Conference in Lithuania
“I have something you need to do for the good of your country.”
“Take one of your gliders, modify it, and fly it across the Atlantic, inspiring students along the way.”
Dr. Rick Spinrad
Assistant Administrator
NOAA
Office of Oceanic and Atmospheric Research

## Slide 9
Longest Mission
in 2006: 500 km
East-West
Distance Across:
5,500 km
RU15
RU27
RU17
Technology Challenges for a Trans-Atlantic Glider Mission
Increase Duration
Ruggedize for Storms
Corrosion & Biofouling
Global Roadmap
RU15 – NJ to Halifax - 2008
RU17 – NJ to Azores - 2008
RU27 – NJ to Spain - 2009
Rutgers
Alumni
Support
Federal Research Agency Response:
Too Risky
for Research

## Slide 11
Scarlet Knight’s Mission Summary
221 days at sea, covering a world record 7,400 km.
Preparing for recovery off
Galicia, Spain
Rutgers students
in the COOLroom
Scarlet
Knight passes the Azores

## Slide 12
Scarlet Knight’s Recovery off of Baiona, Spain

## Slide 13
Scarlet Knight’s Landfall in Baiona, Spain
Same port that Columbus’ Pinta made landfall in 1493

## Slide 14
Scarlet Knight - The first underwater robot to cross an ocean:
A hero’s Welcome, December 9, 2009

## Slide 15
Atlantic Crossing: A Robot’s Daring Mission
An Award-Winning Feature-Length Documentary by Rutgers Filmmaker Dena Seidel
Dena, Fabien Cousteau & Rutgers Students
at the Blue Ocean Film Festival
Filming the recovery of RU27
offshore Baiona, Spain

## Slide 16
Palm Beach Women’s International Film Festival
April 7-10, 2011 www.pbwiff.com
Downtown Boca Film Festival
April 9-17, 2011 www.dbff.us
57 minute TV version distributed
Nationwide to all 350 PBS Stations
on April 29, 2011
Atlantic Crossing: A Robot’s Daring Mission
An Award-Winning Feature-Length Documentary by Rutgers Filmmaker Dena Seidel

## Slide 17
The Scarlet Knight enters the Smithsonian: Dec. 9th, 2010
National Museum of Natural History, Ocean Hall, Washington, DC

## Slide 18: Trans-Atlantic Education
Web Portal
Interactive Data Interface
Google Earth, Glider GUI
Briefing Blog
Social networking tools developed to enable collaboration between scientists and students in the U.S., Canada, Spain and Portugal on the RU15, RU17, and RU27 long-duration glider missions.

## Slide 19: Rutgers Response to the Deepwater Horizon Oil Spill
Web Portal
Briefing Blog
Interactive Data Interface
Google Earth, Glider GUI
Same social networking tools used to coordinate the U.S. National response to the Gulf Oil Spill.

## Slide 20
Deepwater Horizon Oil Spill Response: West Florida Shelf Approaches
10 Gliders Coordinated. 127 Briefs Posted. Several used to brief the White House.
Impacts: (1) We did not get in the way. (2) We reduced the burden.
(3) We informed the Unified Command.

## Slide 21
Global Glider Challenge – The Challenger Mission
December 9, 2009 – Baiona, Spain
HMS Challenger Voyage
First Scientific Circumnavigation
1872-1876
111,000 km =
(15 gliders x 7,400 km/glider)
Rick Spinrad to
Bob Goodman:
Build and Coordinate a Global Glider Fleet to complete the first robotic revisit of the HMS Challenger’s Circumnavigation,
and inspire students along the way.
Bob Goodman to
Rick Spinrad:
We accept
your challenge.

## Slide 22
Challenger Mission – Next Steps – Test Flights
U.S. National Science Foundation’s
Ocean Observing
Initiative:
Education Program for
Sustained at-Sea
Tele-Presence
Spain’s Plataforma Oceanica de Canarias:
Education Program for
Sustained
at-Sea
Human-
Presence
Rutgers Plan for the Challenger Mission:
International Education Program for Sustained
at-Sea Robotic Global Omni-Presence
2011