## Slide 1
UK-IMON International Workshop on New Monitoring Technologies
Theme 2: Autonomous Platforms
Buoyancy Gliders
Scott Glenn,
Oscar Schofield,
Josh Kobut
Rutgers University
Coastal Ocean Observation Lab
http://rucool.marine.rutgers.edu/

## Slide 2
3 Commercial Buoyancy Glider Platforms
Seaglider – Kongsberg
Slocum Glider – Teledyne Webb Research
Spray Glider – Bluefin Robotics

## Slide 3
Glider Flight
Dive: Pump In,
Batteries Forward
Climb: Pump Out, Batteries Back
Rudder for Steering

## Slide 4
Glider Communications
GPS for Position, Iridium for 2-Way, ARGOS for Emergencies
Glider Surfaces
2-Way Satellite Communications in Tail
Data Ribbon Transmitted to Shore

## Slide 5
Glider Sensors
Inside Payload Bay or External

## Slide 6
TRL 5: Independent, third party evaluation or application
that demonstrates reliable long-term field operations?
Rutgers+Partners Glider Deployments since 2003

## Slide 7
U.S. IOOS Real-time Glider Asset Map
U.S. Navy Operational Fleet – 150 Gliders
U.S. IOOS National Glider Network:
U.S. Coastal Deployments since 2003
NSF OOI Glider Fleet – 48 Gliders
U.S. National Glider Activities

## Slide 8
EGO - Everyone’s Gliding Observatories
International Glider Activities
ANFOG – Australian National Facility
Korea – U.S. Polar Gliders
Korea – U.S. Global Gliders

## Slide 9
IMON Criteria: Relevance to requirements of policy, operational and research end users.
GROOM Evaluation: Buoyancy gliders fill a gap left by other observing components.

## Slide 10
Glider Procurement: $130,000 to $175,000
O&M Costs:
Coastal < Boat Day
Global << Ship Day
O&M Tasks | Coastal | Global
Preparation | $14,132 | $24,641
Deployment | $3,329 | $25,041
Piloting | $19,389 | $24,958
Recovery | $3,329 | $22,025
Post deployment | $14,775 | $8,127
Total | $54,954 | $104,793
Cost/day | <$2000 | <$300
Typical Glider Mission Costs
Coastal
1 Month
Global
1 Year

## Slide 11
Summer 2013: Current Mid-Atlantic
Temperature
Glider Data
IMON Criteria:
Multi-purpose?
Hybrid Glider
w/ Propeller
Global Model Forecasts

## Slide 12
Hurricane Irene
August 26, 2011
NOAA/NHC Damage:
#8 with >$15 Billion.
Track Accurate;
Intensity Over-predicted.
Hurricane Sandy
October 29, 2012
NOAA/NHC Damage:
#2 with >$60 Billion.
Track Accurate;
Intensity Under-predicted.

## Slide 13
Brian Powell: Quantifying how observations inform our models
John Wilkin: An evaluation of real-time forecast models of MAB continental shelf waters
Andy Moore: Observations & ocean state estimation: Impact, sensitivity & predictability
Annual ROMS Users Meeting
Rio de Janeiro, 2012
SSH
SST
CTD

## Slide 14
Multiple Goals:
1) provide a unique assimilation dataset for ocean models
2) provide standardized dataset over ecological scales
3) provide information on fish/mammal migrations
4) provide a 3-D snapshot of the MAB cold pool,
5) demonstrate a community surge capacity through the peak fall storms & hurricanes
6) demonstrate data flow from Academics to IOOS to NDBC to GTS via DMAC, and
7) engage undergraduates in ocean observing efforts.
Gliderpalooza
Sept-Oct 2013
Deployments
Penobscot
Blue
RU28
RU23
Otis
RU22
Salacia
OTN201
Saul
OTN200
Darwin
Modena
VIMS
IMON Criteria:
Multi-purpose?
To Date:
13 Gliders,
11 Participants,
11 Funding Sources

## Slide 15
A Global Challenge – The Challenger Glider Mission
December 9, 2009 – Baiona, Spain
HMS Challenger Voyage
First Scientific
Circumnavigation
1872-1876
128,000 km =
= 16 gliders
x 8,000 km/glider
Ralph Rayner & Rick Spinrad’s Global Challenge:
Build a Global Glider Fleet
and Coordinate the First
Robotic Circumnavigation.
Revisit the Historic Track of the
HMS Challenger –
And inspire a global network
of students along the way.

## Slide 16
Glider Silbo, RTOFS & MERCATOR Temperature Sections
Glider Slibo
Mercator
RTOFS
Glider Slibo

## Slide 17
Glider Silbo, RTOFS & Mercator
Temperature and Salinity Time Series
200 m
Salinity
Temperature
800 m

## Slide 18
RTOFS 200m temperature and currents on April 18th, 2013. The glider position is marked by the red dot.
MyOcean 200m temperature and currents on April 18th, 2013. The Gliders position is marked by a red dot.
RTOFS and MERCATOR
Temperature and Current Maps at 200 m

## Slide 19
Global Challenger Glider Mission
16 Global-Class Gliders
5 Ocean Gyres: 16 gliders x 8,000 km/glider = 128,000 km