## Slide 1: Real-Time Beyond the Horizon Vessel Detection
Hugh J. Roarty
Michael Smith
Scott M. Glenn
Donald E. Barrick

## Slide 2: Talk Outline
Introduction to RUCOOL
Introduction of HF radar
Application of HF radar for Search and Rescue (SAR)
Use of HF radar for vessel detection
Real-time results for NY Harbor

## Slide 3
CODAR Network
Glider Fleet
Satellite Data Acquisition Stations
3-D Forecasts
Rutgers University
Coastal Ocean Observation Lab

## Slide 4: Introduction to hf Radar

## Slide 5: CODAR Compact HF Radar Antennas
25 MHz
13 MHz
5 MHz
Combined Transmitter & Receiver
Separate Transmitter & Receiver
FMCW Doppler Radar Average Power 50 watts

## Slide 6: Standard CODAR Shore Site: Shed, Enclosure, Tx/Rx, Comms, Power, GPS, AIS
Enclosure
Shed
monitor
A.C. unit
transmitter
computer & external hard drive
UPS system
receiver
Two lines of Communication
Lightning Protection

## Slide 7: Surface Current Mapping Capability
25 MHz
Radar l: 12 m Ocean l: 6 m
Range: 30 km Resolution: 1 km
13 MHz
Radar l: 23 m Ocean l: 12 m
Range: 80 km Resolution: 3 km
05 MHz
Radar l: 60m Ocean l: 30 m
Range: 180 km Resolution: 6 km

## Slide 8
Mid-Atlantic Bight HF Radar Network
Mid-Atlantic HF Radar Network
16 Long-Range CODARs
8 Medium-Range CODARs
17 Short-Range CODARs
41 Total
Triple Nested & Multistatic
1000 km Alongshore Length Scale

## Slide 9: Winter Storm Nemo
February 9, 2013

## Slide 10: Application of hf Radar to Search and Rescue

## Slide 11
Transition Success Stories – Making a Difference
Optimizing HF Radar for SAR using USCG Surface Drifters
Art Allen
U.S. Coast Guard
Scott Glenn
Rutgers University
Mid-Atlantic Regional Association
Coastal Ocean Observing System

## Slide 12: SAROPS Test Case 5000 Virtual Drifters + 1 Real Drifter (Black Line): Search Area After 96 Hours
HYCOM (Ocean model)
Search Area: 36,000 km2
HF Radar (Measurements)
Search Area: 12,000 km2
232 km
154 km
123 km
100 km
Notes: HYCOM (Low Conf) 48 hours

## Slide 13: hf Radar for Vessel Detection

## Slide 14: Vessel Detection Capability
25 MHz
Range: 11 nmi
Height >10 ft
13 MHz
Range: 43 nmi
Size: >19 ft
05 MHz
Range: 65 nmi
Size: >49 ft

## Slide 15
Doppler Spectra from all Range Cells
with Detection Threshold above Background Applied
Doppler Frequency
(Target Speed)
Range
Bragg Waves
Bragg Waves
Fixed Objects & Direct Signals
Vessel
Vessel

## Slide 16
Step 1
Raw Detections
From each HFR:
Radial Velocity (most accurate)
Range
Bearing (least accurate)
Range (km)
Radial Velocity (m/s)
Bearing (°CWN)

## Slide 17
The Center for Secure and Resilient Maritime Commerce (CSR)
Maritime Domain Awareness
Approach –
Dual Use Technologies
Demonstrate Nested Vessel Detection
Global > Approaches > Port
University of Miami –
Global Satellite Coverage,
Visible & Microwave
Rutgers University –
Over-the-Horizon Compact
High Frequency Radar Networks
Stevens Institute of Technology –
Local High-Resolution Optics &
Shallow Underwater Acoustics
DHS Center of Excellence for Port Security
10 Institutions – Maritime Domain Awareness & Resiliency

## Slide 18: NY HARBOR RECENT RESULTS

## Slide 19: GPS Track YM Los Angeles
Notes: 19

## Slide 20: Pepper Plot
Detections on a Map
Notes: 20

## Slide 21: Association of GPS with Detections
Notes: 21

## Slide 22: NY HARBOR 2012 RESULTS

## Slide 23: Detections Overlaid on AIS
June 11, 2012
06:00-07:00 GMT
Median Background
512 pt. FFT
14 dB SNR detection threshold
13 vessels on AIS

## Slide 24: Detections Overlaid on AIS
June 11, 2012
07:00-08:00 GMT
Median Background
512 pt. FFT
14 dB SNR detection threshold
12 vessels on AIS

## Slide 25
31% of
HF Radar Detections NOT on AIS
Approaches to New York Harbor
16 Vessels per Hour in HFR
5 Vessels NOT on AIS

## Slide 26
Calusa Coast Test Case

## Slide 27
Location Error (km)
0
5
10
15
Intersecting Ranges

## Slide 28: National hf Radar network

## Slide 29: NOAA National Network: Existing Sites
Alaska - 3
Hawaii - 3
CONUS - 104
Puerto Rico - 2

## Slide 30: NOAA National Network: Proposed Sites
Puerto Rico - 20
Pacific Islands - 21
Alaska - 17
CONUS - 262

## Slide 31: Next Steps
Utilize bistatic data
Develop tracker for detections
Questions?
Conclusions
HF radar being used by Coast Guard for Search and Rescue
Can also be used for Maritime Domain Awareness