## Slide 1: Reduced Averaging Times in the Long Range SeaSonde
Hugh Roarty, Chloe Baskin, Michael Smith, Scott Glenn

## Slide 3
Vessels -
Satellite
Satellite
Ships/ Vessels
REMUS
Modeling
Leadership
CODAR
Glider
Data Vis.
Security
Education
CODAR Network
Glider Fleet
Satellite Data Acquisition Stations
3-D Forecasts
Rutgers University - Coastal Ocean Observation Lab
Operations, Research & Education Center

## Slide 4: CODAR Compact HF Radar Antennas
25 MHz
13 MHz
5 MHz
Combined Transmitter & Receiver
Separate Transmitter & Receiver

## Slide 5: Surface Current Mapping Capability
25 MHz
Radar l: 12 m Ocean l: 6 m
Range: 30 km Resolution: 1 km
13 MHz
Radar l: 23 m Ocean l: 12 m
Range: 80 km Resolution: 3 km
05 MHz
Radar l: 60m Ocean l: 30 m
Range: 180 km Resolution: 6 km

## Slide 6
MARACOOS Annual Mean Surface Currents (2012)
Winter
Summer
Spring
Fall

## Slide 7: SeaSonde processing

## Slide 9: Existing SeaSonde Settings
Frequency (MHz) | Sweep Rate (Hz) | Doppler Bins | Time FFT | CSS Avg/Out | Radial Avg/Out | CSS per Radial File
5 | 1 | 1024 | 17m 04s | 60/30 | 180/60 | 5
13 | 2 | 512 | 04m 16s | 15/10 | 75/60 | 7
25 | 2 | 512 | 04m 16s | 15/10 | 75/30 | 7
SeaSonde Acquisition
CSPro
Analyze Spectra
CSQ
CSS
Radial

## Slide 12
1 CSS  98%
3 CSS  96%
5 CSS  92%
7 CSS  86%

## Slide 14: Drifter comparisons

## Slide 17: 3 Hour Radial Averaging

## Slide 18
1 Hour Radial Averaging

## Slide 19
3 Hour
1 Hour
Separation (km)

## Slide 20: 3 Hour Average
169 simulations
3.0

## Slide 21
169 simulations
3 Hour – 23 km
1 Hour – 17 km
26% Drop
1 Hour Average

## Slide 23
197 simulations
3 Hour Average

## Slide 24
197 simulations
1 Hour Average
3 Hour – 19 km
1 Hour – 16 km
16% Drop

## Slide 25
Conclusions
Shorter averaging intervals can increase tidal amplitude measurement
Shorter Averaging intervals led to reduced error in estimate of drifter position
Want to examine effect on uncertainty and coverage