## Slide 1: Quality Control for a Network of High Frequency Radars
Dr. Hugh Roarty
Dr. Scott Glenn
Dr. Josh Kohut
Mr. Michael Smith
Mr. Ethan Handel
Mr. Colin Evans

## Slide 2: Outline
Quality Control on the National Level
Mid Atlantic Structure
Radial Quality Control
Total Quality Control

## Slide 3: 1. Quality control on the national level

## Slide 4: 26 US IOOS core variables
Acidity
Bathymetry
Bottom Character
Colored Dissolved Organic Matter
Contaminants
Dissolved Nutrients
Dissolved Oxygen
Fish Abundance
Fish Species
Heat Flux
Ice Distribution
Ocean Color
Optical Properties
Partial Pressure of CO2
Pathogens
Phytoplankton Species
Salinity
Sea Level
Stream Flow
Surface Currents
Surface Waves
Temperature
Total Suspended Matter
Wind Speed and Direction
Zooplankton Abundance
Zooplankton Species.

## Slide 8
I 2003 December
II 2005 March
III 2005 November
IV 2006 June
V 2009 November
I 2005 February
II 2006 March
III 2007 September
IV 2009 June
V 2011 April
VI 2012 November
VII 2014 March

## Slide 9: 2. MARACOOS HF Radar Network

## Slide 10
To seek, discover & apply new knowledge & understanding
of our coastal ocean
Satellites
HF-Radar
Ocean Forecast Ensemble
Weather Stations
Population Density
Gliders
Drifters
Notes: Need to cut off cold pool in south and bend offshore
Need to experiment with dulling down the colors in the pop density. Maybe orange/tan to white like the box I put in?
Put gliders just below the lines in 3 of them, and increase their angles facing up and down randomly. I stuck in cheesy examples
I already put the shadow and 80% clear line around the two new maps in the upper right, so we are good there.

## Slide 11: MARACOOS HF RADAR NETWORK
 | 5 MHz | 13 MHz | 25 MHz
U Mass |  |  | 
WHOI |  |  | 
U Conn |  |  | 
URI |  |  | 
Stevens |  |  | 
Rutgers |  |  | 
Delaware |  |  | 
ODU/CIT |  |  | 
UNC |  |  | 
9 | 17 | 8 | 17
41 Stations in Total

## Slide 12: Management
Southern
Operator
Northern
Operator
Central
Operator
Regional Coordinator
Hugh Roarty
Distributed Technicians
Chris Jakubiak
Todd Fake
Ethan Handel
Teresa Updyke

## Slide 13: 3. Radial Quality control

## Slide 14: Radial Database
Central location to monitor region
Automatic reprocessing of totals with new radials

## Slide 15: Weekly Site Inspections – 17 Checks

## Slide 16
26 Point Inspection

## Slide 17
11 Point Inspection

## Slide 19: 24 Hour Radial Coverage
http://marine.rutgers.edu/~hroarty/maracoos/radial_coverage/

## Slide 20
Radial Average Bearing
AND
Comparison Between Measured and Ideal Radials
Shore Parallel
Shore Normal

## Slide 21: 13 MHz BRMR Site
BRMR
40°
130°
220°

## Slide 22: Antenna Problem at BRNT Site
Replaced Antenna June 8
BRNT
30°
120°
210°

## Slide 23
Average Radial Velocity
RDLi_BRMR_2012_08_1300
5 cm/s
RDLi_BRMR_2012_08_1400
7 cm/s
RDLi_BRMR_2012_08_1500
10 cm/s

## Slide 26: Radial Inspection Algorithm
Radial Bearing Steady and Shore Normal
24 hour Radial Coverage Test
Load the Radial File
Average Radial Velocity M2 Peak and Power Level
Radial Site Is Cleared for Total Generation
No
No
No
Yes
Yes
Yes

## Slide 27: 4. Total quality control

## Slide 28: 24 Hour Coverage and Mean

## Slide 29: Monthly Coverage and Mean

## Slide 30
Kohut et al. (2012) Ocean Dynamics

## Slide 31
Persistence
UWLS
OI
Persistence
UWLS
OI
Mean Separation
Centroid of Particles and Drifter
95th Percentile Separation
Centroid of Particles and Drifter
Kohut et al. (2012) Ocean Dynamics

## Slide 33: Conclusions
Technicians are the first layer of QC
Algorithms are the second layer
Inspecting total vectors are the third layer