## Slide 1
HF Radar Network (HFRNet)
Data Management and Applications
Lisa Hazard and Hugh Roarty
Scripps Institution of Oceanography and Rutgers University

## Slide 2: Agenda
Overview
Data Acquisition
Site Diagnostics
Data Distribution

## Slide 3: Overview
Years of Operation: 9 years Participating Organizations: 31
Number of files: >7 million Number of Physical Sites: >130

## Slide 4
Network Architecture
Data Acquisition
Example Node to Site Aggregator communications
Example Site Aggregator to Site communications
  Site - the individual field installations of HF radar equipment
  Portal or Site Aggregator - a local regional operations center which maintains multiple installations
  Node - Centralized locations which aggregate data from multiple regions
Notes: We recently changed the name of a “portal” to “Site Aggregator” so it didn’t get confused with a web portal.

## Slide 5
“Portals”
“Node Server”
Scripps and NDBC
West Coast Repository & Engine
“Storage Resource”
Radials and metadata,
Real-time vector (RTV),
graphics
ORB2ORB
RUTGERS
East Coast Repository
ORB2ORB
Web Servers
PUBLIC ACCESS
“Node Server ”
“Portals”

## Slide 6
Diagnostics Radial Diagnostics
Radial diagnostics are summarized in a balloon with a link to the most recent radial image, file information and time histories of latencies and radial solutions

## Slide 7
Diagnostics Network Diagnostics
Network diagnostics are summarized monthly based on file acquisition

## Slide 8
Data Distribution HFRNet Data Availability
Online Visualization – http://cordc.ucsd.edu/projects/mapping/maps/fullpage.php Online visualization of HF radar surface currents with ability to change date, resolution, colorbar, and station information
Web Overlays - http://cordc.ucsd.edu/projects/mapping/api/ Application programming interface (api) that allows programmers to overlay the currents into any website
THREDDS Data Server (TDS) access - http://sdf.ndbc.noaa.gov:8080/thredds/catalog.html http://hfrnet.ucsd.edu/thredds/catalog.html
TDS service that allows folks to acquire or used the data via thredds for processing and/or visualization.
Data Archiving – HFRNet (NDBC): Totals and Radials
      - Operators: Range Series and beam pattern
      - Future: All above through
Notes: When you publish your product, how do you reference SCCOOS?

## Slide 9: 6km grid
Data Distribution
Google Maps Visualization
Features include:
12 zoom levels
Coordinate Locator
Site Diagnostics
Total Vectors at 500m, 1km, 2km & 6km
Hourly and 25 Hour Averaged Data

## Slide 10
http://www.cordc.ucsd.edu/projects/mapping/api/
Data Distribution Google Maps API

## Slide 11
Data Distribution THREDDS
http://hfrnet.ucsd.edu/thredds/catalog.html

## Slide 12
Data Distribution Total Velocities

## Slide 13: Application: Search and rescue

## Slide 14
Application to Search and Rescue
United States Coast Guard
Office of Search and Rescue
Point measurement vs. Field of measurements:
Hurricane Floyd Simulation
Search area reduced by factor of 4 (>10)
O(4)
O(>10)
Courtesy Art Allen, USCG Office of SAR

## Slide 15: 25 MHz Status 2002

## Slide 16
25 MHz Status 2002

## Slide 17: 5 MHz Status 2004

## Slide 18: Status 2004

## Slide 19
2000
2006
2006
2009
2003
2003
2001
2003
2003
2003
2001
2007
2001
LONG RANGE NETWORK
2012
2010
2013
2014

## Slide 20
Vessels -
Satellite
Satellite
Ships/ Vessels
REMUS
Modeling
Leadership
CODAR
Glider
Data Vis.
Security
Education
IOOS Relationships
International Component
National Component
Regional Component
U.S. Integrated Ocean Observing System
Global Ocean Observing System
18 U.S. Federal Agencies
11 Regional Associations

## Slide 21
To seek, discover & apply new knowledge & understanding
of our coastal ocean
Satellites
HF-Radar
Ocean Forecast Ensemble
Weather Stations
Population Density
Gliders
Drifters
Notes: Need to cut off cold pool in south and bend offshore
Need to experiment with dulling down the colors in the pop density. Maybe orange/tan to white like the box I put in?
Put gliders just below the lines in 3 of them, and increase their angles facing up and down randomly. I stuck in cheesy examples
I already put the shadow and 80% clear line around the two new maps in the upper right, so we are good there.

## Slide 22
MARACOOS REGIONAL THEMES & SUCCESS STORIES
2) Ecosystem Decision Support - Fisheries
4) Coastal Inundation - Flooding
5) Energy – Offshore Wind
1) Maritime Operations – Safety at Sea
3) Water Quality – a) Floatables, b) Hypoxia, c) Nutrients
Since 2007

## Slide 23: Themes and Capabilities

## Slide 24
Success Stories – Making a Difference
Optimizing HF Radar for SAR using USCG Surface Drifters
Art Allen
U.S. Coast Guard
Scott Glenn
Rutgers University
and the Mid-Atlantic Regional
Coastal Ocean Observing System

## Slide 25: Search Area After 96 Hours
HYCOM
36,000 km2
CODAR
12,000 km2
232 km
154 km
123 km
100 km
Notes: HYCOM (Low Conf) 48 hours

## Slide 26
May 4, 2009: After a year of testing, NOAA Announces on
U.S. Department of Commerce Website that
MARACOOS CODAR is Operational in SAROPS
U.S. IOOS Goal for 2010-2011:
Bring all
sustained regional-scale HFR networks up to operational status in USCG SAROPS
3 West Coast Regions for
California & Oregon

## Slide 27: HFR Current Mapping Product Development Road Map for Search and Rescue
2002
2003
2004
2005
2006
2007
2008
2009
2010
2011
2012
2013
2014
2015
1998
1999
2000
2001
First Standard Range Codar deployed on East Coast near Atlantic City, NJ
Hurricane Floyd Simulation Predicts Factor of 4 Reduction in Search Area Using Field of Currents vs. Point Measurement
Standard Range Network Proves to be Useful in Coast Guard Research and Development Pilot Study
Long Range Network Shown to be Effective in Second Coast Guard SAROPS tool
MARCOOS Establishes First Regional High Frequency Radar Network
Optimal Interpolation Combination Method Effective in Filling Spatial Gaps in Mid Atlantic Tests
Mid Atlantic HF Radar Network Operational with US Coast Guard
National HF Radar Network Operational with US Coast Guard
Radial and Total Sensitivity Study Undertaken to Provide Best Data to Environmental Data Server
“A Plan to Meet the Nations Surface Current Mapping Needs” Implemented

## Slide 28: Thank You