## Slide 1: Sea Breeze, Coastal Upwelling Modeling to Support Offshore Wind Energy Planning and Operations
Greg Seroka1, Erick Fredj2, Travis Miles1, Rich Dunk1, Josh Kohut1, Scott Glenn1
October 22, 2015 MTS/IEEE OCEANS ‘15
1
2

## Slide 2: Introduction
On November 9, 2015, BOEM commercial lease auction for NJ will take place
  Nearly 344,000 acres for leasing offshore wind (OSW)
  5th competitive lease auction for OSW in U.S.
OSW developer(s) who win a lease zone will submit application to develop to NJ Board of Public Utilities (NJ BPU)
  Must include wind resource assessment & economic analysis

## Slide 3: Introduction
Chart: 2013-14 PJM Mid-Atl. Daily Max Load
Chart: 
| January | February | March | April | May | June | July | August | September | October | November | December
Sea Breeze | 4 | 8 | 13 | 44 | 28 | 39 | 43 | 35 | 29 | 15 | 8 | 2
Upwelling | 0 | 0 | 0 | 0 | 1 | 15 | 46 | 22 | 33 | 6 | 0 | 0
NJ BPU Offshore Wind Rules state:
  “Applications shall account for…the coincidence between time of generation for the project and peak electricity demand.”
Relative Load
NJ sea breeze and coastal upwelling coincident with peak electricity demand
Frequency
Notes: -Sea breeze time of day (afternoon/evening) is also coincident with peak demand time of day (5-7 pm)

## Slide 4
Introduction
Sea breeze
Coastal upwelling
Notes: Cut-out speed of OSW turbines of 4 m/s (calm zone?)

## Slide 5
Coastal upwelling + Sea breeze Hypothesis
Cold upwelling
Does this occur? With or without upwelling?
Introduction

## Slide 6
Key Questions:
What effect does cold coastally-upwelled water have on the coastal/offshore wind resource?
What does the offshore component of the sea breeze look like? Secondary circulation (size, structure)? Offshore divergence?
Introduction
Coastal upwelling
?

## Slide 7: Materials and Methods
Satellite: state-of-the-science declouding and compositing technique designed by Rutgers to determine SST and resolve coastal upwelling
Model: 3km, 600m WRF-ARW 3.6.1; YSU PBL; MM5 Monin-Obukhov surface layer
Advantages (vs. offshore met tower): cost, spatial variability, prediction
Sea Breeze Cases:
July 7, 2013: corkscrew, strong upwelling
July 31, 2014: corkscrew, weak upwelling
April 27, 2013: pure, no upwelling
Coastal upwelling
  Pure
  Corkscrew
  Backdoor
Notes: Satellite: High res in space and time
Previous satellite SST products low in spatial or temporal resolution and are often warmest pixel composites for declouding; cannot resolve coastal upwelling
SST product is IR/near IR (AVHRR); SPoRT is IR/near IR as well
Model: NAM12km for boundary conditions
Cases: largest and longest lasting upwelling in NJ 2012-2014
20140731 case has similar ambient (outside upwelling) water T to 20130707

## Slide 8
Part 1: Coastal upwelling

## Slide 9: Methods
Case 2: July 31, 2014: corkscrew, weak upwelling
Weak upwelling (Actual)
Strong upwelling

## Slide 10
Case 2: 20140731
10m Wind Speed Diff.
100m Wind Speed Diff.
SST Diff.
r2=0.61
r2=0.58
Results
Upwelling produces an inversion, decreasing 10m winds & increasing 100m hub height winds

## Slide 11: Upwelling produces an inversion, decreasing 10m winds & increasing 100m hub height winds
Wind Speed Difference
Case 2: 20140731
Results
10m Wind Speed Diff.

## Slide 12: Upwelling produces an inversion, decreasing 10m winds & increasing 100m hub height winds
Results
10m Wind Speed Diff.
Temperature Difference
Case 2: 20140731

## Slide 13: How will coastal upwelling affect the NJ WEA?
Notes: Could expect similar inversions, impact on 100m winds over upwelling in this structure (affects NJ WEA!)
Need good ocean model to predict this correctly!

## Slide 14
Part 2: Sea Breeze

## Slide 15: Methods
Case 3: April 27, 2013: pure, no upwelling
Lagrangian Coherent Structures (LCSs)
LCSs are boundaries in a fluid that distinguish regions of differing dynamics (e.g. eddies, jets, fronts)
Particles move away from and along a repelling LCS (A), aggregate and move along attracting LCSs (B)
LCS maps identify convergence and divergence in a fluid flow (e.g. sea breeze)

## Slide 16
Benefits of LCS
The Lagrangian measures are advantageous as they are frame independent and robust with respect to localized noise in the data.
Additionally, LCS analysis reveals coherent structures in more detail and with better clarity than streamline plots generated from 2D wind retrieval (Chan and Shao 2007; Tang et al. 2011)
Methods

## Slide 17
LCS Set-up
On 3km WRF winds
1800 UTC to 2300 UTC (peak sea breeze time)
10km grid spacing for tracer trajectories
Perform at these levels in WRF:
  10, 50, 150, 500, 600, 700, 800, 900, 1000, 1500, 2000, 2500m (through marine boundary layer)
Use relative dispersion (RD) to identify LCSs
Methods

## Slide 18
1 km WRF simulation
1500 UTC

## Slide 19
1 km WRF simulation
1800 UTC

## Slide 20
1 km WRF simulation
2100 UTC

## Slide 21
1 km WRF simulation
0000 UTC

## Slide 22
Results
10m

## Slide 23
50m
Notes: Blue red colorbar at +/- 10

## Slide 24
100m

## Slide 25
150m

## Slide 26
500m

## Slide 27
600m

## Slide 28
700m

## Slide 29
800m

## Slide 30
900m

## Slide 31
1000m

## Slide 32
1500m

## Slide 33
2000m

## Slide 34
2500m

## Slide 35: Vertical Cross Section
Top of wind turbine
Coastline
Wind Energy Area Bounds

## Slide 36: Vertical Cross Section
Top of wind turbine
Coastline
Wind Energy Area Bounds

## Slide 37
Divergence is slanted with height, from surface offshore to aloft onshore (agrees with theory)
Reversal in divergence/convergence, and thus approximate height size of sea breeze cell, similar onshore and offshore
  Offshore:
    Divergence: 10 to ~700m
    Convergence: ~700 to 2000m
  Onshore:
    Convergence: 10 to ~600m
    Divergence: ~600 to 1500m
Summary of Part 2 Results

## Slide 38
Hourly LCS RD maps
  Divergence aligned with inland frontal progression?
LCS predictive sea breeze index
  e.g. offshore surface divergence, onshore surface convergence high enough value to get sea breeze? (quick, efficient forecasting method)
3D LCS
  To account for vertical velocities
  For vertical shear analysis (important for wind turbine engineering)
Future Work

## Slide 39
Thank you!

## Slide 40
Extra Slides

## Slide 41: Key Questions
Can we use LCS to more clearly identify and characterize (horizontal & vertical extent, duration, timing, etc.) key structures within the sea breeze (areas of divergence and convergence, fronts, return flow, over water subsidence, calm zones, circulation cells)?
More importantly for offshore wind, can we use LCS to detect areas of higher turbulence and wind shear within the sea breeze, especially offshore?

## Slide 42: Sea Breeze Cases
Case 01: July 7-8, 2013
  Corkscrew, strong upwelling
Case 02: July 31-August 1, 2014
  Corkscrew, weak upwelling
Case 03: April 27-28, 2013
  Pure, no upwelling
  Check 925 mb wind direction for sea breeze type
  Pure
  Corkscrew
  Backdoor

## Slide 43: Sea Breeze Cases
Case 01 and Case 02:
  Results coming soon
Case 03: April 27-28, 2013
  Pure, no upwelling
  Results presented here
  Check 925 mb wind direction for sea breeze type
  Pure
  Corkscrew
  Backdoor

## Slide 44: Case 03: April 27-28, 2013

## Slide 45: WRF Setup
WRF-ARW 3.6.1
3km outer nest, 600m inner nest
North American Mesoscale (NAM) initial and boundary conditions
YSU PBL
  Best PBL scheme for offshore 2m T in UK, no difference for offshore winds (Steele et al 2013)
MM5 Monin-Obukhov surface layer

## Slide 46: Why is RD heterogenous onshore and homogeneous offshore?

## Slide 47
Chart: Speed of Sea Breeze Front (Center) (m/s)
| 0.710219907407407 | 0.750381944444444 | 0.790555555555555 | 0.829328703703704 | 0.872465277777778 | 0.912604166666667 | 0.952743055555556
Time (HH:MM:SS, UTC) | 1.0251 | 0.80116 | 1.7978 | 1.8478 | 1.5992 | 2.0242 | 4.4925
Therefore, speed of sea breeze front is nearly constant between 1900 and 2200 UTC
LCS linear interpolation assumption is validwill gather hourly LCS output to determine temporal evolution of LCS

## Slide 48: More Future Work
Offshore sea breeze extent (i.e. calm zone propagation offshore) sensitivity to PBL scheme?
  YSU 21km, MYNN 0km offshore for one pure sea breeze case (Steele et al 2013)
Apply LCS to scanning LIDAR winds
  Combine with WRF to get back (LIDAR) and forward (WRF) trajectories for real-time structure detection and automated turbulence and wind shear warning system for offshore wind