## Slide 1
Ocean Observing Technologies for Downstream Applications & Services
Scott Glenn & Hugh Roarty
Rutgers University
Academic – Industry Partnerships Since 1998
1st International Congress of New Technology for Sea and River
Barranquilla, Colombia
13-14 October 2016

## Slide 2
Dr. Scott Glenn
Distinguished Professor
MARACOOS Principal Investigator
National HF Radar Steering Committee
glenn@marine.rutgers.edu
Dr. Hugh Roarty
Operations Center Director
MARACOOS HFR Coordinator
Global HF Radar Network Chair
hroarty@marine.rutgers.edu
Rutgers University (RU) Center for Ocean Observation Leadership (COOL) S.Glenn, O.Schofield, J.Kohut, G.Saba, T.Miles, H.Roarty
New Brunswick, New Jersey, USA
http://rucool.marine.rutgers.edu
26 Years of Ocean Observing at:

## Slide 3
CODAR
HF Radar on
Mona Island, Puerto Rico
Today’s Talk:
New Technologies for the many scales of Ocean Observing
HF Radar Applications -
River Plumes, Search And Rescue, Oil Spills & Ports
3) Full Observatory Application - Hurricanes
Trans-Atlantic Glider RU27

## Slide 4
The Ocean is Physically Complex & Biologically Diverse
Global circulation dominated by the Mesoscale
61 Large Marine Ecosystems
Dominated by Coastal Regions

## Slide 5
Vessels -
Satellite
Satellite
Ships/ Vessels
REMUS
Modeling
Leadership
CODAR
Glider
Data Vis.
Security
Education
Global Component
National Component
Regional Component
U.S. Integrated Ocean Observing System (IOOS)
17 U.S. Federal Agencies
11 Regional Associations
http://ioos.gov
15 Regional Alliances in GOOS
Serving Society & Science

## Slide 6
Vessels -
Satellite
Satellite
Ships/ Vessels
REMUS
Modeling
Leadership
CODAR
Glider
Data Vis.
Security
Education
Global Component
National Component
Regional Component
U.S. Integrated Ocean Observing System (IOOS)
17 U.S. Federal Agencies
11 Regional Associations
http://ioos.gov
15 Regional Alliances in GOOS
Serving Society & Science

## Slide 7
A permanent global system for observations, modelling and analysis of marine and ocean variables to support operational ocean services worldwide.
Provides:
-accurate descriptions of the present state of the oceans
(Essential Variables: climate, ocean, biodiversity)
-continuous forecasts of the future conditions of the sea
-the basis for forecasts of climate change
Ocean observations for societal benefit Climate, real time services, ocean health
Notes: This graph to be modified

## Slide 8: Global Ocean Observing System
Needs to be updated…

## Slide 9
https://rucool.marine.rutgers.edu/geohfr/

## Slide 10
https://rucool.marine.rutgers.edu/geohfr/

## Slide 11
WMO/IOC JCOMM
Ocean Glider Working Groups:
Boundary Currents
Storms
Deep Convection
Data Management Cross-cut
Glider Challenge: High resolution for 4D oceanic measurements
WMO/IOC JCOMM Ocean Glider Science/Steering Committee
Intergovernmental Oceanographic Commission

## Slide 12
Vessels -
Satellite
Satellite
Ships/ Vessels
REMUS
Modeling
Leadership
CODAR
Glider
Data Vis.
Security
Education
Global Component
National Component
Regional Component
U.S. Integrated Ocean Observing System (IOOS)
17 U.S. Federal Agencies
11 Regional Associations
http://ioos.gov
15 Regional Alliances in GOOS
Serving Society & Science

## Slide 13: The U.S. National Science Foundation’s Ocean Observatories Initiative
Computer Science Component:
Manish Parashar, Ivan Rodero
+
Ocean Observing Component:
S. Glenn, O. Schofield,
M. Crowley & M. Vardaro
=
Cyber-Oceanography
Rutgers University
New Brunswick, NJ

## Slide 14
OOI’s 7 Arrays: UW, WHOI, OSU
Endurance
Cabled
4 Global
Pioneer

## Slide 15
OOI By the Numbers
Arrays
4 Global, Pioneer, Endurance, Cabled
Sites
Moorings, Profilers, Nodes
Mobile Assets
Gliders, AUVs
Instruments
Science Data Products
Science/Engineering Data Products
7
50
33
>900
>2500
>100K

## Slide 16
Serving Science & Education:
Oceanobservatories.org
Ooinet.oceanobservatories.org
Education.oceanobservatories.org
OOI Data Management, Quality Control & Web Access: Rutgers

## Slide 17
Vessels -
Satellite
Satellite
Ships/ Vessels
REMUS
Modeling
Leadership
CODAR
Glider
Data Vis.
Security
Education
Global Component
National Component
Regional Component
U.S. Integrated Ocean Observing System (IOOS)
17 U.S. Federal Agencies
11 Regional Associations
http://ioos.gov
15 Regional Alliances in GOOS
Serving Society & Science

## Slide 18
U..
Cape
Cod
Cape
Hatteras
NJ
MA
CT
VA
DE
NY
NC
RI
MD
PA
78 Million People (1/4 of U.S.)
1000 km Cape to Cape
Middle Atlantic
Regional Association
Coastal
Ocean Observing System
MARACOOS:
A Sustained Real-time Observation & Forecast System
>40 PIs
>20 Institutions
>50 Members
>2000 Contacts
Scott Glenn + Many
Notes: 18

## Slide 19
The Global Ocean Observing System
Regional Alliance for the Wider Caribbean
Report on IOCARIBE-GOOS to the
XII Intergovernmental Session of IOCARIBE
12-14 April 2013, Panama
Submitted by W. Douglas Wilson
IOCARIBE-GOOS Project Coordinator
Founding Co-Chairman of IOCARIBE-GOOS
Group of Experts and Steering Committee

## Slide 20
Coastal Colombia:
Two ~1000 km
Regional Segments
840 km
670 km

## Slide 21
HYCOM- Navy

## Slide 22: RTOFS

## Slide 23
OSCAR

## Slide 24
Global Drivers
Coastal Population Centers
International Commerce
Ocean Seasonality
Tropical Cyclones

## Slide 25
MID-ATLANTIC REGIONAL DRIVERS
Ocean Circulation
Tropical Storms
Population
Ports
Northeasters
Climate Change
Critical Habitat

## Slide 26: Colombia Drivers

## Slide 27: South America Hurricane Tracks

## Slide 28
MARACOOS REGIONAL RESPONSE THEMES
2) Ecosystem Decision Support - Fisheries
4) Coastal Inundation - Flooding
5) Energy – Offshore Wind
1) Maritime Operations – Safety at Sea
3) Water Quality – a) Floatables, b) Hypoxia, c) Nutrients

## Slide 29
Real-Time Satellite Ground Stations in the Northeast U.S.
Rutgers
Johns Hopkins
U. Delaware
City College of N.Y.
U. Maine
Satellites: NOAA Polar Orbiters, NPP, Terra, Aqua, Metop & GOES
Industry
Partner

## Slide 30
SST Products – coldest pixel composite
Coldest pixel SST composite used to retain coastal upwelling & storm mixing processes
Steps to creation:
Clean up AVHRR scans
  Remove sun glint, data close to edge
Decloud (specific to MAB)
  AVHRR Channel 2 (0.725-1 μm) tests:
    Remove if near IR albedo > 2.3%
    Remove if Δnear IR albedo > 0.15% within 3km x 3km box
  AVHRR Channel 4 (10.3-11.3 μm) tests:
    Remove if T < 5°C (summer), 3.5°C (winter)
    Remove if ΔT > 1°C within ~3km x 3km box
3-day coldest pixel composite with NASA SPoRT 2km SST
  Keep only coldest pixel between SPoRT SST and 12-21 UTC AVHRR scans
    AVHRR Channel 2 needs daytime
Coastal upwelling
Hurricane cooling
Notes: seroka

## Slide 31
Mid-Atlantic Bight HF Radar Network
Mid-Atlantic HF Radar Network
17 Long-Range CODARs
7 Medium-Range CODARs
17 Short-Range CODARs
41 Total CODARs in Region
+5 CODARs outside Region
46 Total CODARs
Triple Nested, Multi-static, Multi-use
Industry Partner: CODAR Ocean Sensors
1000 km
Cape to Cape

## Slide 32
Grid Points for USCG 80-80 Metric
U.S. Coast Guard
HF Radar Metric
Total Current Vectors:
80% Spatial Coverage
80% of the Time
USCG SAR Grid
National HFR Grid

## Slide 33
2008
2009
2010

## Slide 34: Resilient CODAR Shore Site: Shed, Enclosure, Tx/Rx, Comms, Power, GPS, AIS
Enclosure
Shed
monitor
A.C. unit
transmitter
computer & external hard drive
UPS system
receiver
Two lines of Communication
Lightning Protection

## Slide 35
HFR Network Design Example:
1000 km / ( 75 km/segment )
= 13 Segments of Coast
Acquisition & Installation and
Annual Technician Support cost
estimates based on the U.S.
National HF Radar Network
design parameters.
Segment Color Key
Red > 90 km
90 km > Orange > 70 km
70 km > Green
Active Spares Approach
Spares used to fill the largest gaps.
Improve data quality when all are running.
Improve network resiliency when one site goes down.

## Slide 36
MARACOOS Exceeds USCG 80-80 Metric
Through Improved Site Resiliency & Active Spares
With 1/2 of the U.S. IOOS Recommended Technician Support

## Slide 37
Mid-Atlantic Bight Glider Network
Satellite Ocean Color
Satellite SST
Subsurface
Glider
Data
RU01
RU15
RU29
Industry Partner: Teledyne Webb Research
G1
G1-Ruggedized
G2

## Slide 38
Glider Sensors
Inside Payload Bay or External

## Slide 39
Global Challenger Glider Mission: South Atlantic 2013-2016

## Slide 40
Rapid Response Glider Development
Rapid Response Glider (v1)
Un-pumped Seabird Conductivity Temperature Depth (CTD), Wetlabs ECOpuck (CDOM, Chlorophyll, Backscatter), Aandera Optode (Oxygen).
Rapid Response Glider (v2)
Pumped CTD, Externally mounted Nortek Aquadopp Current Profiler, integrated accelerometer, extended battery bay, Thruster G1.
Rapid Response Glider (v3)
Integrated current profilers, expanded capacity buoyancy pumps, thruster G2, integrated LISST-200X particle sizer (sediment, oil droplet, phytoplankton, etc.).
Notes: Need ONR and GoMRI

## Slide 41
Deepwater Horizon Oil Spill: U.S. Environmental Protection Agency required that LISSTs are equipped on all vessels used for monitoring the oil spill.
  LISST measurements used for measuring the size and concentration of dispersed oil droplets.
  Size of oil droplets as input to NOAA models to predict water column position and plume distribution.
New Sensor development: Integration into Teledyne-Webb Slocum gliders with real-time data telemetry.
  Capabilities will include particle size distribution and concentrations (sediment, phytoplankton, oil droplets)
  10 Science bays currently being built for global scale deployments of opportunity.
http://www.sequoiasci.com/article/deepwater-horizon-oil-spill-in-the-gulf-of-mexico/

## Slide 42
MARACOOS Weather Network
NDBC
Backbone
> 50 sites
Regional Industry
Enhancement
> 100 sites

## Slide 43: Atmospheric Modeling: Rutgers University Weather Research and Forecasting (RU-WRF) Model
Triple nested: 9-3-1km
  9km: 0, 6, 12, 18Z cycles
  3km: 0, 12Z cycles
  1km: 12Z cycle
3-hourly forecast: out to 5 days (9km), 2 days (3km) and 1 day (1km)
Initial Conditions:
  9km: 0.25 degree GFS
  3km: 4km NAM
  1km: RU-WRF 3km
Boundary Conditions:
  9km: 0.25 degree GFS
  3km: RU-WRF 9km
  1km: RU-WRF 3km
Version: 3.7.1
Physics options: (New Thompson microphysics; MYNN2 PBL; no cumulus parameterization; RRTMG LW, New Goddard SW radiation; MYNN surface layer; NOAH land surface model, NOAH UCM urban physics, Simple Ocean Mixed Layer)
Satellite SSTs: state-of-the-science declouded coldest pixel composite SST to resolve coastal upwelling and storm mixing

## Slide 44
Bottom temperature
Data used [… real-time SOURCE] *THREDDS Data Server
72-hour forecast NAM 0Z cycle at 2 am EST [NCEP NOMADS]
RU regional CODAR hourly: 4-hour latency delay [RU TDS*]
RU glider T,S when available (~ 1 hour delay) [RU TDS]
USGS daily average flow available 11:00 EST [USGS waterdata]
AVHRR IR passes 6-8 per day (~ 2 hour delay) [MARACOOS TDS]
REMSS MW-IR blended SST daily average [NASA PO-DAAC]
HYCOM NCODA 7-day forecast updated daily [NRL]
Jason-2, CryoSat, AltiKa along-track altimeter OGDR [RADS.nl]
SOOP XBT/CTD, Argo floats, on GTS [NOAA OSMC ERDDAP]
Rutgers ROMS 4DVAR uses all available data from a modern coastal ocean observing system
  more and diverse data is better (T, S, u, sea level)
  bias correction to OBC and MDT is essential
Useful subsurface skill for real-time applications:
  4 days for temperature and salinity;
  1-2 days for velocity
Future directions: variational methods for observing system design; coupling; ecosystems
4-day forecast
2-day forecast
Data assimilation analysis/hindcast
Forward model after bias removal
Forward model
depth
correlation

## Slide 45
Data assimilative modeling, with nesting, for forecasting and reanalysis in the MAB and Gulf of Maine with ROMS
With NASA OSTST (D. Vandemark, UNH) and NSF OOI (A. Moore UCSC)
** It’s a double espresso
Scope of the existing ESPreSSO* real-time forecast and reanalysis ROMS system
*Experimental System for Predicting Shelf and Slope Optics
All available in situ IOOS and satellite data are assimilated using 4DVAR
Scope of new Doppio** real-time/reanalysis system
Notes: From Wilkin
The present Rutgers ROMS real-time forecast model (ESPreSSO) spanning the MAB has been operating since late 2009 with 4D Variational (4DVAR) data assimilation of all available MARACOOS observations (CODAR, gliders) and satellite (altimeter, SST).
Of 7 real-time modeling systems evaluated that cover the MAB, no model is more skillful (Wilkin and Hunter, JGR, 2013).
The system produces a 72-hour forecast every day.
To better represent upstream conditions to the MAB, and to serve the needs of Marine Fisheries users in the Gulf of Maine and Georges Bank, a new system is under development (Doppio) with an expanded domain, and numerous enhancements to the assimilation procedure and data streams.

## Slide 46
CODAR Network
Glider Fleet
Satellite Data Acquisition Stations
3-D Forecasts
Rutgers - Center for Ocean Observation Labs:
MARACOOS Operations Lab

## Slide 47
Rutgers - Center for Ocean Observation Labs:
Global Ocean Education Lab

## Slide 48
Regional Priority Themes | Regional Observation & Modeling Capabilities |  |  |  |  | 
 | Weather Mesonet | HF Radar Network | Statistical STPS | Satellite Imagery | Glider Surveys | Dynamical Ocean Forecasts
Theme 1. Maritime Safety | Operational Input to USCG SAROPS | Operational input to USCG SAROPS | Operational input to USCG SAROPS | SST for survivability planning | Assimilation dataset for forecast models | Surface currents for SAROPS
Theme 2. Ecological Decision Support | Weather forecast ensemble validation | Circulation and divergence maps for habitat |  | SST & Color for habitat | Subsurface T & S for habitat | 3-D fields of T, S, circulation for habitat
Theme 3. Water Quality | Winds for transport, river plumes, & upwelling | Surface currents for floatables, bacteria, spill response | Surface currents for floatables, bacteria, spill response | Ocean color for river plumes | Nearshore dissolved oxygen surveys | Surface currents for floatables, bacteria, spill response
Theme 4. Coastal Inundation | Weather forecast ensemble validation | Current forecast model validation |  | SSTs assimilation into forecast models | Assimilation dataset for forecast models | Nested forecast ensembles
Theme 5. Offshore Energy | Historical analysis & wind model validation | Historical current analysis & wind model validation |  | Historical analysis surface fronts & plumes for siting | Historical analysis of subsurface fronts & plumes | Coupled ocean-atmosphere models for resource estimates
Integration Matrix: Capabilities Support Multiple Themes

## Slide 49
Regional Priority Themes | Regional Observation & Modeling Capabilities |  |  |  |  | 
 | Weather Mesonet | HF Radar Network | Statistical STPS | Satellite Imagery | Glider Surveys | Dynamical Ocean Forecasts
Theme 1. Maritime Safety | Operational Input to USCG SAROPS | Operational input to USCG SAROPS | Operational input to USCG SAROPS | SST for survivability planning | Assimilation dataset for forecast models | Surface currents for SAROPS
Theme 2. Ecological Decision Support | Weather forecast ensemble validation | Circulation and divergence maps for habitat |  | SST & Color for habitat | Subsurface T & S for habitat | 3-D fields of T, S, circulation for habitat
Theme 3. Water Quality | Winds for transport, river plumes, & upwelling | Surface currents for floatables, bacteria, spill response | Surface currents for floatables, bacteria, spill response | Ocean color for river plumes | Nearshore dissolved oxygen surveys | Surface currents for floatables, bacteria, spill response
Theme 4. Coastal Inundation | Weather forecast ensemble validation | Current forecast model validation |  | SSTs assimilation into forecast models | Assimilation dataset for forecast models | Nested forecast ensembles
Theme 5. Offshore Energy | Historical analysis & wind model validation | Historical current analysis & wind model validation |  | Historical analysis surface fronts & plumes for siting | Historical analysis of subsurface fronts & plumes | Coupled ocean-atmosphere models for resource estimates
Integration Matrix: Capabilities Support Multiple Themes

## Slide 50
Regional Priority Themes | Regional Observation & Modeling Capabilities |  |  |  |  | 
 | Weather Mesonet | HF Radar Network | Statistical STPS | Satellite Imagery | Glider Surveys | Dynamical Ocean Forecasts
Theme 1. Maritime Safety | Operational Input to USCG SAROPS | Operational input to USCG SAROPS | Operational input to USCG SAROPS | SST for survivability planning | Assimilation dataset for forecast models | Surface currents for SAROPS
Theme 2. Ecological Decision Support | Weather forecast ensemble validation | Circulation and divergence maps for habitat |  | SST & Color for habitat | Subsurface T & S for habitat | 3-D fields of T, S, circulation for habitat
Theme 3. Water Quality | Winds for transport, river plumes, & upwelling | Surface currents for floatables, bacteria, spill response | Surface currents for floatables, bacteria, spill response | Ocean color for river plumes | Nearshore dissolved oxygen surveys | Surface currents for floatables, bacteria, spill response
Theme 4. Coastal Inundation | Weather forecast ensemble validation | Current forecast model validation |  | SSTs assimilation into forecast models | Assimilation dataset for forecast models | Nested forecast ensembles
Theme 5. Offshore Energy | Historical analysis & wind model validation | Historical current analysis & wind model validation |  | Historical analysis surface fronts & plumes for siting | Historical analysis of subsurface fronts & plumes | Coupled ocean-atmosphere models for resource estimates
Integration Matrix: Capabilities Support Multiple Themes

## Slide 51
“An Interdisciplinary Process Study
of the Hudson River Plume
in a Sustained Coastal Observatory”
LaTTE
Principal Investigators
Physics
Bob Chant (Rutgers)
Bernie Gardner (U. Mass)
Scott Glenn (Rutgers)
Bob Houghton (Lamont)
John Wilkin (Rutgers)
Chemistry
John Reinfelder (Rutgers)
Bob Chen (U. Mass)
Biology
Paul Bissett (FERI)
Tom Frazer (U. Florida)
Mark Moline (Cal-Poly)
Oscar Schofield (Rutgers)
Meng Zhou (U. Mass)
Plus Many Others
Lagrangian Transport & Transformation Experiment
Dye Release Studies –
May 2004 Pilot: 1/3, 2/3 Split
April 2005 High Flow: 2 Injections
May 2006 Follow-up: 1 Injection
Coastal Observatory Sponsors

## Slide 53
The Nearshore Recirculation: An Incubator for Phytoplankton
Observatory Finds
The Frazer Eddy!
Hudson River
Drifters Recirculate
Large
Phytoplankton
Dominate
Oxygen Drops

## Slide 54
Freshwater Plume moves Cross-Shelf, down the Hudson Shelf Valley
Satellite SST
Long-Range CODAR
Surface Currents
Glider Salinity Section
Glider Track
Deploy
The
Robot
Kerfoot et al
OS45D-21

## Slide 55
Shipboard Salinity Section
Across the NJ Coastal Current
and the HSV Highway
LaTTE 2005 -- After Luring the Cape Hatteras Offshore.
“The survey began on the ‘Highway’. We were near the glider when it surfaced. We saw currents ripping southward in a 10 m thick layer of freshwater along the highway -- perhaps the most significant freshwater transport we saw all week.”
“Perhaps the most perplexing to me is ‘the Highway’ and why there has been a lack of a strong coastally trapped flow this week.”
--- Bob Chant aboard the Cape Hatteras, April 21, 2005

## Slide 56
Mid-Atlantic Bight HF Radar Network
Mid-Atlantic HF Radar Network
17 Long-Range CODARs
7 Medium-Range CODARs
17 Short-Range CODARs
41 Total CODARs in Region
+5 CODARs outside Region
46 Total CODARs
Triple Nested, Multi-static, Multi-use
Industry Partner: CODAR Ocean Sensors
1000 km
Cape to Cape

## Slide 57
Success Stories – Making a Difference
Optimizing HF Radar for SAR using USCG Surface Drifters
Art Allen
U.S. Coast Guard
Scott Glenn
Rutgers University
Mid-Atlantic Regional Association
Coastal Ocean Observing System

## Slide 58: Self-Locating Data Marker Buoy (SLDMB) Deployments 1 Jan 2006 – 31 Dec 2007
Notes: Here are the initial deployment positions for our SLDMBs. From these records we selected only those that exceeded 4 days in length

## Slide 59
Can HF Radar provide improved estimates of the location of SLDMB?
USCG Search And Rescue
Status 2004

## Slide 60
Can HF Radar provide improved estimates of the location of SLDMB?
USCG Search And Rescue
Status 2004

## Slide 61
Transition Objective –
Operational Use of HF Radar Surface Currents for Search And Rescue
Surface Currents
Search And Rescue Optimal Planning System (SAROPS)
Data Acquisition
Data Product Generation & Management

## Slide 62: 5000 Virtual Drifters – Search Area After 96 Hours
HYCOM
36,000 km2
CODAR
12,000 km2
232 km
154 km
123 km
100 km
Notes: HYCOM (Low Conf) 48 hours

## Slide 63
May 4, 2009: After a year of testing, NOAA Announces on
U.S. Department of Commerce Website that
MARACOOS CODAR is Operational in SAROPS
2009-2010 Activity:
Bring all
sustained regional-scale HFR networks up to operational status in USCG SAROPS
3 West Coast Regions for
California & Oregon are ready.

## Slide 64
Madrid
Deepwater
Horizon
Loop Current -----> Gulf Stream
Rutgers
U.S. IOOS Response to the Gulf of Mexico Oil Spill:
The Critical Role of Modern Ocean Observing Networks
Scott Glenn,
Representing
Many IOOS &
DHS Partners
Many
Sponsors,
Including
National Center for
Secure and Resilient
Maritime Commerce
RU27
Silbo

## Slide 65
2010 Deepwater Horizon Oil Spill
Oil Transport Questions: Will the oil….
Come ashore in Louisiana?
Spread east to Texas or west to Mississippi, Alabama and Florida pan handle in the wind-driven coastal currents?
Enter the Loop Current and be transported downstream?
Hit the Florida Shelf and be driven shoreward by winds?
Ride the Loop Current south and hit the Florida Keys?
Be transported out of the Gulf of Mexico by the Gulf Stream and impact the East Coast?
Gulf of Mexico

## Slide 66
22
23
24
25
26
27
28
Sea Surface Temperature (⁰Celsius)
Glider
Gliders
Drifters
Argo Floats
HF Radar
Deepwater Horizon Incident: IOOS assets

## Slide 67
Responding to Crisis: Deepwater Horizon
U.S. IOOS partnership demonstrated ability to:
Quickly deploy technologies: Gliders and HF radar, saving resources/improving safety
Models/Imagery ingested into NOAA/Navy models
Data assimilation improved spill response decision-making and public understanding
USM HFR
USF HFR
Web Portal
HFR data informed NOAA
trajectory forecasts
Briefing Blog
127 Briefs
HFR validation of SABGOM Forecast combined with satellite detected oil slicks
June 2

## Slide 68
Near Field Environmental Analyses: Wind Shift – Strong Winds & Waves from SE
June 29
July 3
July 7
July 4

## Slide 69
Approach to West Florida Shelf: Asset Maps, HFR, Gliders, HyCOM
June 3
June 4

## Slide 70
July, 2009
August, 2009
September, 2009
Extreme Far Field:
East Coast Risk Assessments:
HFR Fields from 2009
June 25
July 6

## Slide 71: Feedback from the Deepwater Horizon Incident Command Center
“…Thanks to everyone for all of your efforts to support the Response and the very professional and competent manner in which you have executed your efforts. IOOS has played a huge role in informing the modeling teams and the Unified Command through your extraordinary service. “
- Sam Walker (IOOS representative to Deepwater Horizon Unified Command Center), August 6, 2010
“… AWESOME JOB - that call that we had last week was a very good thing. You are taking a huge burden off of the team here who is trying to simply capture the deluge of assets now being deployed. “
- Sam Walker (IOOS representative to Deepwater Horizon Unified Command Center), July 2, 2010
“All - Greetings from Unified Area Command in New Orleans. I couldn't agree more - the IOOS community has acquitted itself very well during this entire incident. Not only has everyone provided valuable information - you have done it without getting in the way of the ongoing operations. It's been a pleasure to represent IOOS here and see all the great contributions from the larger IOOS community. “
- Sam Walker (IOOS representative to Deepwater Horizon Unified Command Center), June 18, 2010
Composite of Satellite Observed Oil Spill Locations

## Slide 72: Feedback from the Deepwater Horizon Incident Command Center
“…Thanks to everyone for all of your efforts to support the Response and the very professional and competent manner in which you have executed your efforts. IOOS has played a huge role in informing the modeling teams and the Unified Command through your extraordinary service. “
- Sam Walker (IOOS representative to Deepwater Horizon Unified Command Center), August 6, 2010
“… AWESOME JOB - that call that we had last week was a very good thing. You are taking a huge burden off of the team here who is trying to simply capture the deluge of assets now being deployed. “
- Sam Walker (IOOS representative to Deepwater Horizon Unified Command Center), July 2, 2010
“All - Greetings from Unified Area Command in New Orleans. I couldn't agree more - the IOOS community has acquitted itself very well during this entire incident. Not only has everyone provided valuable information - you have done it without getting in the way of the ongoing operations. It's been a pleasure to represent IOOS here and see all the great contributions from the larger IOOS community. “
- Sam Walker (IOOS representative to Deepwater Horizon Unified Command Center), June 18, 2010
Composite of Satellite Observed Oil Spill Locations
We did not get in the way
We reduced the burden
We informed modeling teams & leadership
DHS S&T Impact Award

## Slide 73
www.legislative.noaa.gov/Testimony/Lubchenco033111.pdf
From Page 10:
Also in support of oil spill response, NOAA requests a $5.0 million increase to implement the U.S. Integrated Ocean Observing System (IOOS®) Surface Current Mapping Plan using high frequency (HF) radar surface current measurements. HF radar provides information vital to oil spill response, national defense, homeland security, search and rescue operations, safe marine transportation, water quality and pollutant tracking, and harmful algal bloom forecasting.

## Slide 74
Hurricane Irene
August 28, 2011
NOAA/NHC Damage:
#7 with >$16 Billion.
Track Accurate;
Intensity Over-predicted.
Hurricane Sandy
October 29, 2012
NOAA/NHC Damage:
#2 with >$68 Billion.
Track Accurate;
Surge Under-predicted.
Avila & Cangialosi, 2012, Tropical Cyclone Report
Georgas et al., 2014, J. of Extr. Even.
Colle et al., 2015, J. Mar. Sci. & Engr.

## Slide 75
U..
Cape
Cod
Cape
Hatteras
78 Million People (1/4 of U.S.)
1000 km Cape to Cape
Middle Atlantic
Regional Association
Coastal
Ocean Observing System
Irene
Sandy
Stratified
Coastal Ocean Interactions with
Tropical Cyclones
Arthur
Scott Glenn, Travis Miles,
Greg Seroka, Robert Forney,
Hugh Roarty, Oscar Schofield, Josh Kohut (Rutgers),
Yi Xu (China) & Fei Yu (China)
Nature Communications (2016)
Barry
Hermine
Notes: 75

## Slide 76
Over 2 million people ordered to “flee the storm’s path”.
President Obama: Shaping up to be a “historic hurricane” and urged residents to “be prepared for the worst”. “Don’t wait. Don’t delay.”
New Jersey Governor Christie: Ordered evacuation of 1 million people - “Get the hell off the beach”. “Do not waste any more time working on your tan”.
New York Mayor Blumberg: “Staying behind is dangerous, staying behind is foolish, and its against the law”. “The time to leave is right now”. The bridges, streets and subways were nearly empty ahead of a nearly unprecedented mass transit shutdown.
Pre-Irene Storm Warnings

## Slide 77
Post-Irene Analysis:
Track accurately forecast
days in advance.
Intensity (wind speed), and the resulting impacts, were over-predicted.
Close the Intensity Science Gap!

## Slide 78
Production Suite Review: December 4, 2012
Motivation: Research to Operations to Research (R2O2R)
Track Error: Decreases in 20-Year Trend Intensity Error: - “Long-term trend is flat”
Track: Improvements attributed to Global Forecast Models & the Super-Ensemble.
Intensity: “…upper-ocean thermal structure can affect the evolution of storm intensity, …Unfortunately, the paucity of subsurface measurements limits our ability to assess the effect of upper-ocean variability on tropical cyclone intensity evolution.”
– Emanuel et al., (2004)

## Slide 79
Hurricane Irene
August 27-28, 2011
Two Gliders Deployed
NOAA/NHC:
Damage >$16B ( #7)
Track Accurate
Intensity Over-predicted

## Slide 80
Hurricane Irene
August 27-28, 2011
Two Gliders Deployed
14
33
29
105
60
salinity
% oxygen
temperature
55
55
0
0
55
depth
depth
depth
8/12
9/07
date
26
0
Hurricane Irene
NOAA/NHC:
Damage >$16B ( #7)
Track Accurate
Intensity Over-predicted

## Slide 81
Temp. Vert. Vel.
Temp. Vert. Vel.
Temp. Vert. Vel.
RU16
Temp.
Section
Upcast
Downcast

## Slide 82
For Each 2-hour Segment:
1) Calculate the Average Temperature Profile
2) Calculate the Vertical Velocity Standard Deviation Profile and Smooth Vertically.
Pre-Irene
During Irene
Post-Irene
Temp
S.D. w’

## Slide 83
WHAT?
Satellite
SST
Post-Irene
Pre-Irene
Difference
WHY?
HF Radar
Currents
WHEN? Glider Temperature
Eye Passage
11C max Cooling
?

## Slide 84
WHAT?
Satellite
SST
Post-Irene
Pre-Irene
Difference
WHY?
HF Radar
Currents
WHEN? Glider Temperature
Eye Passage
11C max Cooling

## Slide 85
ROMS Model Results at Glider Location
Coastal Baroclinic Circulation Enhances Mixing & Cooling

## Slide 86
ROMS Model Cross-shelf Section: SST cooling, downwelling bottom T
Downwelling
Upwelling
Seroka et al. in prep.
AOEC SST cooling
Notes: 10

## Slide 87
Seroka et al. in prep.
m s-2
+offshore
-onshore
ROMS Model Cross-shelf Section: onshore WS vs. offshore PG
Notes: 15

## Slide 88
Modeled Deepwater Cooling Processes in Hurricane Irene
Air-Sea Only
1-D Mixing
3-D PWP (Upwelling)

## Slide 89
Observed Cooling in Hurricane Irene
Ahead-of-Eye-
Center Cooling:
Water Temp
Air Temp
Air Press
Wind Speed

## Slide 90
Ahead of Eye Center Cooling
Left: U.S. Mid-Atlantic
Right: East China & Yellow Seas
AOE Center Cooling in Buoy Record:
Mid Atlantic Average: 75%
Super-typhoon Muifa: 85%
See Glenn et al., Nature Comms, 2016
11 Hurricanes since 1985
26 Typhoons since 1985

## Slide 91
Rutgers Atmospheric Forecast Sensitivity Study
Warm Ocean
Boundary Condition
Cold Ocean
Boundary Condition
IMPACT?
>10 knots reduction in peak wind speed
Cat 1 Hurricane
Tropical Storm

## Slide 92
26C
SST within 25 km of eye & impact on air-sea heat flux
Warm
Cold
Northern Buoy
Central Buoy

## Slide 93
NARR
WARM SST
COLD SST
Wind
Latent heat flux
Sensible heat flux
WRF Heat Flux Comparison to
North American Regional Reanalysis

## Slide 94
NARR
WARM SST
COLD SST
WRF 250-850 hPa Wind Shear
August 28
00:00 Z
August 28
12:00 Z

## Slide 95
NARR
WARM SST
COLD SST
WRF Dry air intrusion (700 mb specific humidity)
August 28
00:00 Z
August 28
12:00 Z
Notes: SST sensitivity is not affecting or not being affected by humidity

## Slide 96
WRF Model Sensitivity Study
Over 130 model runs
Paired to compare sensitivities
Central pressure & max wind
Sensitivity to SST greatest
Seroka, Miles, Xu, Kohut, Schofield & Glenn,
Hurricane Irene Sensitivity to Stratified Coastal Ocean Cooling, Monthly Weather Review, 2016

## Slide 97: Improved satellite SST product revealed ahead-of-eye cooling was not captured by:
BEFORE IRENE
AFTER IRENE
HWRF-POM
low res
MARACOOS SST
RTG HR SST
NAM model
standard satellite product
ocean models used for forecasting hurricane intensity
HWRF-HYCOM
medium res
Notes: Caveats: different atmospheric forcing, etc.
Rutgers SST: 2km, RTG: 1/12 deg, ~9 km, HWRF-POM: 18km, HWRF-HYCOM: 1/12 deg, ~9km

## Slide 98
Hurricane Hermine Response: CINAR/MARACOOS Glider Fleet Launched, 9/2016
Glider
HYCOM
RTOFS

## Slide 99
Hurricane Hermine Response: CINAR/MARACOOS Glider Fleet Launched, 9/2016
Glider RU30
HYCOM
RTOFS

## Slide 100
Hurricane Irene Track August 27-28, 2011
Summary:
Summer Storm
Strong Stratification
Coastal Response
Mixing Cooled Surface
Limited Intensity

## Slide 101
UWA
2nd IO
SKLECR
IO
KIOST
BIOS
CariCOOS
UPRM
UVI
TWR
AOML
MARACOOS/CINAR
UMaine
WHOI
UMass
Rutgers
UMaryland
VIMS
NCEP
Growing Tropical Cyclone Global Glider Network
Now JCOMM Ocean Glider Working Group #2: Storms
USP
UCT
Selected EGO Goals from Pierre Testor, Slide 4:
Coordination of ongoing research, and the conception of future research
Build Capacity to operate fleets of gliders at international level
USM
NRL
NTU
BMKGA

## Slide 103
Hourly maps of the surface current velocity can be viewed for the previous 24 hours (observed currents) and next 24 hours (predicted tidal currents)
Each point is clickable and will bring up time series plots of observed and predicted speed and direction (pictured)
Text output of time series will also be available
Searchable to find nearest grid point to entered latitude and longitude values
NOAA NOS CO-OPS
PORTS System
High Frequency RADAR
Surface Currents
http://tidesandcurrents.noaa.gov/hfradar/

## Slide 104: HF Radar Monitors Nearshore Waves
National Waves Plan
Nearshore HF Radar product
Validation with a NOAA Buoy
Codar at Breezy Pt.
Significant Wave Height (m)
NOAA Buoy 44025
13 New Buoys in
Mid Atlantic

## Slide 105: HF Radar Detects Tsunamis
6 km offshore
10 km offshore
14 km offshore
18 km offshore
22 km offshore
Long Beach Island, NJ

## Slide 106: 2013 High Frequency Radar Class @ University of Puerto Rico Mayaguez

## Slide 107
National HF Radar Network in South Africa
HF Radar Course at University Cape Town 2015
HF Radar Deployment with SA Navy
National Planning Workshop 2014
Intensive Classroom & Field Program followed by Skype Sessions

## Slide 108
Lessons Learned:
Establish Noble Goals
Academic–Industry–Government Partnerships accelerate development.
Integration Matrix approach to Implementation
Free, Open & Sustained Access to Quality Data
Products Serve Multiple Societal & Science Needs
Workforce Training is Essential