## Slide 1
Mike Crowley, Kelly Knee, Mike Smith, Laura Nazzaro, Hugh Roarty, Matt Oliver, Gerhard Kuska, Josh Kohut, Scott Glenn
September 19, 2017 MTS Anchorage
Data QA/QC in the IOOS Mid-Atlantic Regional Association Coastal Ocean Observing System

## Slide 2: The next 18 minutes
Overview of MARACOOS
Data access points
Data Management
QA/QC of gliders, HF-Radar and satellite data
QA/QC of external data sets
Take Home Message:
MARACOOS is a government certified data provider that performs QA/QC on ocean data products and makes them freely available through oceansmap.maracoos.org as well as a comprehensive THREDDS server.
MTS 2017 Anchorage
crowley@Rutgers.edu

## Slide 3: NOAA-led U.S. Integrated Ocean Observing System (IOOS)
Vessels -
Satellite
Satellite
Ships/ Vessels
REMUS
Modeling
Leadership
CODAR
Glider
Data Vis.
Security
Education
Global Component
National Component
Regional Component
17 U.S. Federal Agencies
11 Regional Associations
15 Regional Alliances in GOOS
MTS 2017 Anchorage
crowley@Rutgers.edu

## Slide 4: NOAA-led U.S. Integrated Ocean Observing System (IOOS)
MTS 2017 Anchorage
crowley@Rutgers.edu
U..
Cape
Cod
Cape
Hatteras
NJ
MA
CT
VA
DE
NY
NC
RI
MD
PA
10 States - 76 Million People
1000 km Cape to Cape
Middle Atlantic
Regional Association
Coastal
Ocean Observing System
MARACOOS:
An Integrated, Sustained & Certified Real-time Observation System
501(c)3 association
25 universities
21 state/federal government agencies
18 private sector partners
12 non-governmental entities

## Slide 5: Data Access: MARACOOS.org
MTS 2017 Anchorage
crowley@Rutgers.edu

## Slide 6: Oceansmap.maracoos.org
MTS 2017 Anchorage
crowley@Rutgers.edu

## Slide 7: MARACOOS Certification
MARACOOS’ ability to achieve and consistently maintain federal data quality standards led to its certification as a Regional Information Coordination Entity (RICE) in December 2016.
What does that all mean?
MTS 2017 Anchorage
crowley@Rutgers.edu
Assures users that MARACOOS data meet or exceed federal standards for quality (names names!)
Ensures that the data collected and distributed by the RICE are managed according to the best practices, as identified by NOAA.
MARACOOS.org/certification

## Slide 8: MARACOOS Data Mgmt & Communication (DMAC)
The system includes:
management of in situ & remotely-sensed observation and model** data
data-model connections for comparison
data access services such as Thematic Real-time Environmental Distributed Data Services (THREDDS), Open-source Project for a Network Data Access Protocol (OPeNDAP)
common data formats such as NetCDF
delivery of data to operational users
MTS 2017 Anchorage
crowley@Rutgers.edu
**Note: models are not certified

## Slide 9: Data Assembly Center
The DAC includes:
data generated by MARACOOS partners (eg. Gliders)
data collected by non-partner organizations such as the Hudson River Environmental Conditions Observing System (HRECOS)
data from government providers: NDBC, CO-OPS, NERRS, USGS, CBIBS
MARACOOS data is delivered to national data assembly centers (DACs) (GliderDAC and the National HF-RADAR Network).
MTS 2017 Anchorage
crowley@Rutgers.edu

## Slide 10: Data
MTS 2017 Anchorage
crowley@Rutgers.edu

## Slide 11
MTS 2017 Anchorage
crowley@Rutgers.edu
There are MANY types. Today we are focusing on:
High Frequency Radar (HF Radar)
Ocean Gliders
Advanced Very High Resolution Radiometer (AVHRR),
Hudson River Environmental Conditions Observing System (HRECOS)

## Slide 12: HF-Radar
MTS 2017 Anchorage
crowley@Rutgers.edu

## Slide 13
Mid-Atlantic HF Radar Network
17 Long-Range CODARs
8 Medium-Range CODARs
16 Short-Range CODARs
41 Total CODARs in Region
+5 CODARs outside Region
46 Total CODARs
Hourly currents
Industry Partner: CODAR Ocean Sensors
HF-Radar

## Slide 14: CODAR Coverage:
MTS 2017 Anchorage
crowley@Rutgers.edu
Long Range (6km) Medium Range (2.5km) Short Range (1km)

## Slide 15
HF-Radar: Radials vs Vectors
Radials Total Vectors

## Slide 16
HF-Radar: Required QARTOD QC
All required QARTOD tests are enabled.

## Slide 17
From
QARTOD
Manual for
HF Radar
HF-Radar: QARTOD QC Tests

## Slide 18
National HF-Radar Network
All data are archived through the national network
Hfradar.ndbc.noaa.gov

## Slide 19: Underwater Gliders
MTS 2017 Anchorage
crowley@Rutgers.edu

## Slide 20: Gliders
MTS 2017 Anchorage
crowley@Rutgers.edu
MARACOOS leverages Teledyne Webb Slocum Gliders

## Slide 21: Glider Flexibility
MTS 2017 Anchorage
crowley@Rutgers.edu
Acoustic Modem
ADCP/DVL
Altimeter
Bathyphotometer (bioluminescence)
Beam Attenuation Meter
Echo Sounder
Optical Backscatter
Optical Attenuation
Oxygen
Conductivity, Temperature, Depth
Fish Tracking
Fluorometer
Hydrocarbon
Hydrophones
Nitrates
PAR sensor
Radiometer
Scattering Attenuation Meter
Spectrophotometer (red tide)
Turbulence
Wave Accelerometer
Internal Payload Bay
External Mounted
Internal
External Payload Area

## Slide 22: Glider Data QA/QC
EPA Quality Assurance Project Plan:
Glider Mission Planning
SeaBird CTD
Aanderra Optode 3835
Documents for pre- and
post- deployment glider, CTD and DO QA
QARTOD
MTS 2017 Anchorage
crowley@Rutgers.edu

## Slide 23: Required Real-Time QARTOD Tests
Timing/Gap Test: data received in the expected time window
Syntax Test: data able to be translated to meaningful values
Location Test: data measured in the geographically expected location
Gross Range Test: valid instrument measurement range
  Pressure
  Temperature
  Conductivity
  Salinity
Pressure Test: monotonic increase/decrease in pressure records over the profile
MTS 2017 Anchorage
crowley@Rutgers.edu

## Slide 24: Strongly Recommended Real-Time QARTOD Tests
Performed on Pressure, Temperature, Conductivity and Salinity
Climatological Test: values fall in an expected range. Currently, global values are used, but plans to use local ranges are in the works.
Spike Test: capture individual spikes in variable records. Large values marked as failing while smaller values marked as suspect.
Rate of Change Test: marks improbable time-based rate of change between successive records.
Flat Line Test: marks continuously repeated observations of the same value.
MTS 2017 Anchorage
crowley@Rutgers.edu

## Slide 25: Suggested Real-Time QARTOD Tests
Future work, with the exception of #5, due to the relative sparseness of real-time data sets. May be implemented on delayed mode data sets in the future.
Multivariate Tests
Attenuated Signal Tests
Previous Profile Test
TS Curve/Space Test
Density Inversion Test
MTS 2017 Anchorage
crowley@Rutgers.edu

## Slide 26: National Glider DAC
T/S Product Visualizations: https://gliders.ioos.us/map/
MTS 2017 Anchorage
crowley@Rutgers.edu

## Slide 27: AVHRR Satellite Data
MTS 2017 Anchorage
crowley@Rutgers.edu

## Slide 28: Satellites – MARACOOS Receiving Stations

## Slide 29: AVHRR SST Data Workflow
Dish
Satellite Raw Data
TeraScan
R
NCDF-3 Output SST
MARACOOS TDS
De-cloud/masking reprojection; Output NCDF-4
  Available products
    Single Pass Aggregation: Annual aggregations of single passes, 2013 to present
    Single Pass Individual Files: individual satellite passes, 2013 to present
    1-day-Aggregation: annual aggregations of 1-day composites from 2013 to present
    1-Day Individual Files: individual 1-day composites from 2013 to present
    3-day-Aggregation: annual aggregations of 3-day composites from 2013 to present
    3-Day Individual Files: individual 3-day composites from 2013 to present
    7-day-Aggregation: annual aggregations of 7-day composites from 2013 to present
    7-Day Individual Files: individual 7-day composites from 2013 to present

## Slide 30: AVHRR SST: Automated QC Tests
Time Test: A measurement fails the time test if it is more than 2 degrees cooler than the mean of the satellite passes in the previous 72 hrs.
Climatology Test: A measurement fails if the temperature is more than 5 degrees colder than the climatologies from the NSIPP AVHRR Pathfinder and Erosion Global 9km SST Climatology.
Sequential time and climatology test: In this test, the previous 72 hours of satellite passes are first passed through a climatology test, then passed through the time test. It is a sequential test, rather than two independent tests.
Remember, data are flagged, NOT removed

## Slide 31: AVHRR SST: Experimental Cloud Masking
Remember, data are flagged, NOT removed
Comparing satellite SST measurements with NDBC SST measurements.
205 sites compared, Jan 1, 2006 – September 14, 2014.
Additional visual inspection of each data set
For each site, a root mean square (RMS), bias and observation number statistic was calculated. only pixels that passed all tests), failed only the time test, or failed only the climatology test are kept in the regional de-clouding process.

## Slide 32: AVHRR – de-Clouded SST products
Comparing de-Clouded AVHRR to~200 NDBC buoys and platforms
De-Clouding
NDBC 41001 as an example
(red dots satellite, black NDBC buoy
De-Clouding night imagery
MTS 2017 Anchorage
crowley@Rutgers.edu

## Slide 33: U.S. IOOS is…
MTS 2017 Anchorage
crowley@Rutgers.edu
External: Hudson Rivers Environmental Conditions Observing System
(HRECOS)

## Slide 34: What is HRECOS
MTS 2017 Anchorage
crowley@Rutgers.edu
Continuous meteorological and water quality monitoring stations on the Mohawk and Hudson Rivers since 2008
Operated by a consortium of government, academic, and private institutions.
All stations operate year-round except the Mohawk at Ilion station due to seasonal drawdown in the canal
Data: water temperature, specific conductivity, salinity (calculated from specific conductivity and temperature), dissolved oxygen, depth, water elevation, pH, turbidity, air temperature, barometric pressure, relative humidity, wind speed, wind direction, radiation, and rainfall, collected at 15 min intervals.

## Slide 35: HRECOS Initial QC
MTS 2017 Anchorage
crowley@Rutgers.edu
Continuous meteorological and water quality monitoring stations on the Mohawk and Hudson Rivers since 2008
operated by a consortium of government, academic, and private institutions.
All stations operate year-round except the Mohawk at Ilion station due to seasonal drawdown in the canal
Data: water temperature, specific conductivity, salinity (calculated from specific conductivity and temperature), dissolved oxygen, depth, water elevation, pH, turbidity, air temperature, barometric pressure, relative humidity, wind speed, wind direction, radiation, and rainfall, collected at 15 min intervals.
The HRECOS QAPP describes the objectives and criteria and specifies the measures and corrective actions used to ensure data quality.
Goal: accept at least 90% of total possible observations
Water quality sensors and weather stations are recalibrated if they do not meet the standards specified in the QAPP.
The data flags used for the automated real-time data flagging process are summarized in Table 1 and apply to all parameters.
Flag Value | Definition
0 | Acceptable data
5 | Data that demonstrate a significant increase or decrease from the previous value
6 | Flat-lined data
30 | Data outside three standard deviations of the seasonal mean
40 | Data outside four standard deviations of the seasonal mean
100 | Data outside the range of the instrument

## Slide 36
Quarterly Review
Missing data added
The recorded data is also reviewed and flagged
Recalculates automatic flags using actual seasonal averages,
Run SOPs based on their documentation
Makes a final determination for the public record by applying the final flag values
Flag Value | Definition
0 | Data determined to be acceptable after a final review by the site manager
10000 | Suspicious data according to a final review by the site manager
20000 | Corrected data
500000 | Rejected data according to a final review by the site manager
HRECOS Final QC

## Slide 37: Overview of Real-Time & Quarterly Process
MTS 2017 Anchorage
crowley@Rutgers.edu
HRECOS has both an automated real-time flagging process and a manual quarterly process in place

## Slide 38: Summary
MTS 2017 Anchorage
crowley@Rutgers.edu
So much data, and all available for public use
Only an example of numerous datasets from partners available
Any piece of this talk could have been a single 20 minute presentation
Today, examples of single platform, multi-platform, Federal Government and external data QC were presented
Thanks to US IOOS, my co-authors and the dozens of people that support the MARACOOS project
Certified data! We Certify our own through QARTOD, SOPs, and confirm that external data have a QA/QC process in place. Otherwise data is “citizen science”
Maracoos.org, Oceansmap.maracoos.org
crowley@Rutgers.edu

## Slide 40: U.S. IOOS is…
MTS 2017 Anchorage
crowley@Rutgers.edu
Level 0
Level 1
Level 2
Level 3
HF Radar Data Flow Chart
Level 4
Green – Operational
Orange – Development
Red - Planned
Data levels defined by NASA Earth Science Reference Handbook ( 2006, p.31)
Manufacturer recommended Antenna Patterns not older than 1 year
Comparison of radar velocity with in situ drifters
Weekly 11-point remote site inspections
Physical site inspection every 6 months
Quality Control Steps
QARTOD
  Global range test (300 cm/s)
  Local range Test (by station)
  Stuck sensor (0.01 cm/s / 3 hours)
  Gradient (18 cm/shr)
  Spike (0.1 cm/s )
Filter based on manufacturer supplied uncertainty parameters
Human-in-the-loop visual inspection of radial data
Global range test (300 cm/s)
Filter based on uncertainty values for each optimal interpolation vector after Kohut (2012)
Discrete Cosine Transform spatial filter after Fredj (2016)
Frequency
GPS Alignment
Visible Bragg
Interference
Sea Echo Phases
Forward/ Reflected Power
Terminal Errors
Chasis Temperature
Computer Memory Space
Ideal radial generatin
Measured radial generation