## Slide 1
Integrated Ocean Observing Systems &
Applications to Hurricanes & Typhoons:
1) HF Radar & Irene + 10 + Muifa
Scott Glenn
2) Gliders & Sandy + Jose
Travis Miles
Rutgers University, New Brunswick, NJ, USA
Third DBCP Pacific Islands Training Workshop on
Ocean Observations and Data Applications
Fifth JCOMM Marine Instrument Workshop for Asia-Pacific Region
Hai Kou China, 09-12 July 2018

## Slide 2: U.S. Integrated Ocean Observing System (IOOS)
  Global Component
  US contribution to Global Ocean Observing System (GOOS)
  1 of 15 Regional Alliances of GOOS
  National Component
  17 Federal agencies
Regional Component
  11 Regional Associations
    Stakeholder driven
    Academia, state/local/tribal government, private industry
Partnership effort that leverages dispersed national investments to deliver ocean, coastal and Great Lakes data relevant to decision-makers.
Notes: NOAA is the Lead Federal Agency
US IOOS program office is within NOAA, but intended to be a multi agency network and federal to non-federal so we use the term U.S. IOOS.
Additional Background:
US IOOS is a national endeavor and spans from global to coastal, with federal and non-federal partners. The majority of non-federal partners are represented by 11 Regional Associations (RAs) that represent the US EEZ and Great Lakes.

## Slide 3
U..
Cape
Cod
Cape
Hatteras
Mid-Atlantic Bight (1000 km Cape to Cape)
78 Million People (1/4 of U.S.)
A Sustained, Integrated & Certified
Ocean-Atmosphere
Observation & Forecast System
Mid-Atlantic Regional Association Coastal Ocean Observing System (MARACOOS)
Notes: 3

## Slide 4
46 Site CODAR Network
Under-
water
Glider
Fleet
Satellite Receivers
Ocean
Forecasts
Rutgers University - Center for Ocean Observing Leadership
Glider Lab
Notes: 4
All of this gets combined into our overall operations, research, and educational initiatives in the “COOL Room,” shown here (with a class in the background)
Thanks to many partners

## Slide 5
46 Site CODAR Network
Under-
water
Glider
Fleet
Satellite Receivers
Ocean
Forecasts
Rutgers University - Center for Ocean Observing Leadership
9km
3km
1km
RU-WRF Domains
Atmospheric Forecasts
Notes: 5
All of this gets combined into our overall operations, research, and educational initiatives in the “COOL Room,” shown here (with a class in the background)
Thanks to many partners

## Slide 6
Weathertight SeaSonde Enclosure
monitor
A.C. unit
transmitter
computer & external hard drive
UPS system
receiver
two lines of Communication
lightning protection
13 MHz Transmit and Receive Antenna
4 m
Doppler shift gives ocean currents
SeaSonde
HF Radar

## Slide 7
25 MHz
Radar l: 12 m Ocean l: 6 m
Range: >30 km Resolution: 1 km
13 MHz
Radar l: 24 m Ocean l: 12 m
Range: >80 km Resolution: 3 km
05 MHz
Radar l: 60m Ocean l: 30 m
Range: >180 km Resolution: 6 km
Individual HF Radar Sites
Generate Radial Vector Surface Current Maps

## Slide 8
Radial Current
Vectors from Multiple Sites
Combined into Total Vectors
by UWLS or OI

## Slide 9
Mid-Atlantic Bight HF Radar Network
Generates Total Vector Surface Current Maps
Mid-Atlantic HF Radar Network
17 Long-Range CODARs
8 Medium-Range CODARs
16 Short-Range CODARs
41 Total CODARs Fixed
+5 CODARs Roaming
46 Total CODARs
Triple Nested, Multi-static, Multi-use
Industry Partner: CODAR Ocean Sensors
1000 km
Cape to Cape

## Slide 10
HFR Data Quality Assurance/Quality Control (QA/QC)
Plotting QC flags in real time
From
QARTOD
Manual for
HF Radar
Regional Information Coordination Entity -
RICE

## Slide 11: HF Radar Data Real Time Flow Chart
Level 0
Nov. 2017
Data levels defined by NASA Earth Science Reference Handbook ( 2006, p.31)
Level 1
Level 2
Level 3
Level 4
Green – Operational
Yellow – Development
Red - Planned
Quality Assurance
Manufacturer recommended Antenna Patterns not older than 1 year
Weekly 11-point remote site inspections
Physical site inspection every 6 months
QARTOD
R Test 1: SNR Ratio, Filter < 7dB
S Test 2: Cross Spectra Covariance Matrix Eigenvalue
S Test 3: Direction of Arrival Magnitude
S Test 4: Direction of Arrival Signal Width
S Test 5: Positive Definiteness 2x2 Signal Matrix
R Test 6: Syntax, Filter
R Test 7: Max Threshold, Filter > 150 cm/s (13/25 MHz) 300 cm/s (5 MHz)
R Test 8: Radial Valid Location, Filter
D Test 9: Radial Count, Filter < 300
S Test 10: Spatial Median Test
S Test 11: Temporal Gradient
S Test 12: Average Radial Bearing
S Test 13: Synthetic Radial
R Test 14: Data Density Threshold, Filter, At least 3 vectors from 2 separate stations
R Test 15: GDOP, OI Uncertainty, Flag > 0.6 in U or V Velocity
R Test 16: Max. Speed Threshold , Filter > 150 cm/s (13/25 MHz) 300 cm/s (5 MHz)
S Test 17: Spatial Median Test
Requires SeaSonde Radial Metric Processing
R Required
SR Strongly Recommended
S Suggested
D Development
For IOOS HFR DAC

## Slide 12: Radial Web Server
Rutgers COOLroom CODAR Wall
Human in the Loop QA/QC

## Slide 13: Radial Diagnostic
Displays Most Recent Radial File
Displays Preferred Radial Type for Total Processing
If radial file older than 12 hours
If radial count drops below 200

## Slide 14: HF Radar Data Delayed Mode Flow Chart
Level 0
Nov. 2017
Data levels defined by NASA Earth Science Reference Handbook ( 2006, p.31)
Plot hardware diagnostic data to identify questionable time periods.
Plot radial diagnostic data to identify questionable time periods.
Determine what stations need to be reprocessed for specific time periods
Generate reprocessing time line with appropriate file type (ideal or measured) and antenna patterns.
Generate archived best radial data set.
Create totals from best radial data set.
Level 1
Level 2
Level 3
Level 4
Green – Operational
Yellow – Development
Red - Planned
For NCEI Archive

## Slide 15
5 MHz- 17 Stations
13 MHz- 7 Stations
25 MHz- 16 Stations
Outside- 6 Stations
TOTAL – 46 Stations
Winter Storm Jonas
2016/01/23 20:00 UTC
Delayed-mode
Post-processed Maps to NCEI Archive
for Scientific Analysis:
ex., Decadal Mean Currents
Near Real-Time
Hourly Maps for
Search And Rescue,
Water Quality,
Spill Response, …
Mid-Atlantic Bight HF Radar Network
Generates Surface Current Maps every hour for over a decade

## Slide 16
U.S. National HF Radar Network
Search And Rescue Optimal Planning System
(SAROPS)

## Slide 17: Search And Rescue Data Availability Metrics
MARACOOS 17-Site Long Range Network:
Consistently exceeds U.S. Coast Guard 80-80 Metric
80 % spatial coverage 80% of the time
Achieved through site resiliency and active spares approach.
Accomplished with 2.5 Field Technicians
Every
6 Months since 2007

## Slide 18
HFR Data
Navy HYCOM Region 1
2016 Surface Current Drifter Skill Score
National Search and Rescue School
Yorktown, VA
January 19, 2017
Coast Guard Sector NY
Staten Island, NY
March 21, 2017
Active Education & Outreach to USCG Users of the HFR Data & Data Assimilative Products
No HFR Assimilation

## Slide 19: Coast Guard Wind & Current Data Requests
USCG SAROPS requests June 1 to December 1, 2017

## Slide 20
WMO & IOC JCOMM Global HF Radar Network

## Slide 21
Promoting the Global Network through Education & Training

## Slide 22
U..
Cape
Cod
Cape
Hatteras
Mid-Atlantic Bight (1000 km Cape to Cape)
78 Million People (1/4 of U.S.)
Irene + 10
Sandy
Stratified
Coastal Ocean Response and Feedbacks on Hurricane Intensity
Jose
Scott Glenn, Travis Miles,
Joe Brodie, Cliff Watkins,
Greg Seroka, Hugh Roarty,
Oscar Schofield, Josh Kohut (Rutgers)
Notes: 22

## Slide 23
Key Storm Glider Reference List
Glenn, Jones, Twardowski, Bowers, Kerfoot, Kohut, Webb, Schofield, 2008. Glider observations of sediment resuspension in a Middle Atlantic Bight fall transition storm. Limnology and Oceanography 53(5, Part 2): 2180-2196.
Miles, Glenn, Schofield, 2013. Temporal and spatial variability in fall storm induced sediment resuspension on the Mid-Atlantic Bight. Continental Shelf Research 63, Supplement: S36-S49.
Miles, Seroka, Kohut, Glenn, 2015. Glider observations and modeling sediment transport in Hurricane Sandy. JGR Oceans, DOI: 10.1002/2014JC010474
Glenn, Miles, Seroka, Xu, Forney, Yu, Roarty, Schofield, Kohut, 2016. Stratified coastal ocean interactions with tropical storms, Nature Communications, March 8, 2016, 1-10, DOI:10.1038/ncomms10887.
Seroka, Miles, Xu, Kohut, Schofield & Glenn, 2016. Hurricane Irene Sensitivity to Stratified Coastal Ocean Cooling, Monthly Weather Review, 144(9) 3507-3530.
Seroka, Miles, Xu, Kohut, Schofield & Glenn, 2017. Rapid shelf-wide cooling response of a stratified coastal ocean to hurricanes. JGR-Oceans: Special Section on Ocean Responses and Feedbacks to Tropical Cyclones, DOI:10.1002/2017JC012756.
Miles, Seroka & Glenn, 2017. Coastal ocean circulation during Hurricane Sandy, J. Geophysical Res. - Oceans, 122(9) DOI:10.1002/2017JC013031.
Air-Sea Interface
Sea-Bottom Interface

## Slide 24
Hurricane Irene
August 28, 2011
NOAA/NHC Damage:
>$16 Billion.
Track Accurate;
Intensity Over-predicted.
Hurricane Sandy
October 29, 2012
NOAA/NHC Damage:
>$68 Billion.
Track Accurate;
Surge Under-predicted.
Avila & Cangialosi, 2012, Tropical Cyclone Report
Georgas et al., 2014, J. of Extr. Even.
Colle et al., 2015, J. Mar. Sci. & Engr.

## Slide 25
Hurricane Irene
26-29 August 2011
Super-Typhoon Muifa
26 July - 9 August 2011
Hurricane Irene & Super-Typhoon Muifa:
What do these summer of 2011 storms have in common?
Track was accurate, Intensity was over-predicted

## Slide 26: Earth’s northern mid-latitude sea surface temperatures (SSTs) undergo large seasonal cycles
Summer-Winter SST Difference (1995-2005)
Schofield et al. 1998
Ramya Ramadurai, 2009
Notes: Earth’s northern mid-latitudes undergo large seasonal cycles, not only in the atmosphere but also in the ocean. Within the ocean, this seasonal cycle is especially pronounced over the western continental boundaries often characterized by broad continental shelves and proximity to coastal population centers [Schofield et al., 2008].
Figure 1. Global ocean temperature contrast between winter and summer months, which were designated based on the mean seasonal temperatures
measured with the AVHRR satellite. Data were taken between 1995 and 2005. The grey shades on the land masses indicate human
populations (dark grey = high human populations).

## Slide 27
Mid Atlantic
Winter (1-layer)
Mid Atlantic
Summer (2-layers)
Cold Pool
To characterize the Cold Pool, we need ocean observations that are “fit for purpose”
Essential Ocean Feature - Mid-Atlantic’s Cold Pool
An unseen cold bottom layer beneath a warm summer surface layer
Assimilated into Regional
Ocean Models
Satellite SST
Glider Zig-Zags
or Triangles
Bottom Temperature

## Slide 28
Mid Atlantic
Winter (1-layer)
Mid Atlantic
Summer (2-layers)
Cold Pool
Why unseen? Satellites cannot see below surface, Argo Floats do not extend into shallow water
Mid- Atlantic’s Cold Pool
Yellow Sea’s Cold Bottom Water Mass
Yellow Sea
Summer
Yellow Sea
Summer
Cold Bottom Water Mass
Cold Bottom Water Mass
Essential Ocean Feature - Mid-Atlantic’s Cold Pool
An unseen cold bottom layer beneath a warm summer surface layer

## Slide 29
WHAT?
Satellite
SST
Post-Irene
Pre-Irene
Difference
WHY?
HF Radar
Currents
WHEN? Glider Temperature
Eye Passage
11C max Cooling
Essential Ocean Processes:
Ahead of eye center – Vertical Shear > Mixing > Cooling

## Slide 30
Summer Tropical Cyclones Tracks over the Continental Shelf
11 Hurricanes since 1985
26 Typhoons since 1985

## Slide 31
Hurricanes Crossing the MAB in Stratified Season
Observed Ahead-of-Eye-Center Cooling (NDBC)
Super-Typhoons crossing the Yellow Sea in Stratified Season
Observed Ahead-of-Eye-Center Cooling (Fei Yu & Yi Xu)

## Slide 32
WRF Atmospheric Forecast Sensitivity Study – >130 tests
Warm Ocean
Boundary Condition
Cold Ocean
Boundary Condition
IMPACT?
>10 knots reduction in peak wind speed
Cat 1 Hurricane
Tropical Storm

## Slide 33
Hurricane Irene –
WRF Model Sensitivity Study
Over 130 model runs
Paired to compare sensitivities
Central pressure & max wind
Sensitivity to SST greatest
Monthly Weather Review (2016)
Notes: This shows that, for the first time in 30 years there is the potential to dramatically increase forecast intensity at landfall, by including

## Slide 34
Hurricane Irene
Direct Wind Forcing
Inertial Response

## Slide 35
Mixed Layer Depth from HF radar
(Pollard and Millard, 1974; Cliff Watkins, Ph.D. Thesis)
Hurricane Irene:
P&M 1974: Simple model uses mixed layer depth & wind to predict inertial amplitude
CW 2018: Invert model to use forecast wind & HF Radar inertial amplitude to predict mixed layer depth

## Slide 36
Two types of coastal ocean response
to Mid Atlantic hurricanes discovered
The essential ocean features are
  Seasonally warmed surface water
  Persistent Cold Pool bottom water.
The essential ocean processes are
  (a) ahead-of-eye mixing/cooling
  (b)
The essential ocean impacts on the atmosphere are
  (a) ocean mixing/cooling reduces storm intensity - Irene
  (b)
New Scientific Understanding:
+ Monthly Weather Review (2016)
+ JGR-Oceans (2017)
+ JGR-Oceans (2017)

## Slide 37
NOAA Historical Hurricane Tracks: 1851 - previous season
Upper Ocean Heat Content modulates Hurricane Intensity

## Slide 39
I
IOCARIBE
> GOOS
MARACOOS
> IOOS > GOOS
http://global-hfradar.org/
WMO/IOC JCOMM Global HF Radar Network

## Slide 40
CODAR SeaSondes in the Gulf of Mexico: Existing

## Slide 41
CODAR SeaSondes in the Gulf of Mexico: Existing+Proposed
Cabo San Antonio
La Havana

## Slide 42
Typhoon and Tropical Cyclone Tracks: Asia-Pacific Region

## Slide 43
WMO/IOC JCOMM Global HF Radar Network:
Asia-Pacific Region

## Slide 44
Program
Surface Currents, HF Radar Networks, Antenna Distortion, Doppler Spectra, Surface Waves, Tsunami and Data Sharing
http://orca2018.official.jp/

## Slide 45
The Ocean we need for the Future we want:
Enhancing sustainable use of ocean and marine resources
Expanding use of knowledge about the ocean conditions
Supporting the development of the ocean economy
Sustainable management of coastal ecosystems
Increasing scientific knowledge
Achieving integrated observations and data sharing - GOOS
Intergovernmental
Oceanographic
Commission (IOC):
“2nd Ocean Decade”
Planning Phase
2018-2021
Thank
You