## Slide 1: Two Decades (1998-2018) of Surface Current Measurements on the Mid Atlantic Continental Shelf
Hugh Roarty Josh Kohut Mike Smith Laura Nazzaro
Ethan Handel
Travis Miles
Joe Brodie
Scott Glenn
Calypso
April 18, 2018
Qawra, Malta
Larry Atkinson
Teresa Updyke
Donglai Gong
Harvey Seim
Mike Muglia
Wendell Brown

## Slide 2
U..
Cape
Cod
Cape
Hatteras
NJ
MA
CT
VA
DE
NY
NC
RI
MD
PA
10 States - 78 Million People
1000 km Cape to Cape
Middle Atlantic
Regional Association
Coastal
Ocean Observing System
MARACOOS:
An Integrated, Sustained & Certified Real-time Observation and Forecast System
Notes: 2

## Slide 3
CODAR Network
Glider Fleet
L-Band & X-Band Satellite Receivers
3-D Nowcasts
& Forecasts
Rutgers University - Coastal Ocean Observation Lab
Observatory Operations, Data Fusion & Training Center
Notes: 3

## Slide 4
Regional Priority Themes | Regional Observation & Modeling Capabilities |  |  |  |  | 
 | Weather Mesonet | HF Radar Network | Statistical STPS | Satellite Imagery | Glider Surveys | Dynamical Ocean Forecasts
Theme 1. Maritime Commerce & Safety | Operational Input to USCG SAROPS | Operational input to USCG SAROPS | Operational input to USCG SAROPS | SST for survivability planning | Assimilation dataset for forecast models | Surface currents for SAROPS
Theme 2. Fisheries | Weather forecast ensemble validation | Circulation and divergence maps for habitat |  | SST & Color for habitat | Subsurface T & S for habitat | 3-D fields of T, S, circulation for habitat
Theme 3. Public Health & Water Quality | Winds for transport, river plumes, & upwelling | Surface currents for floatables, bacteria, spill response | Surface currents for floatables, bacteria, spill response | Ocean color for river plumes | Nearshore dissolved oxygen surveys | Surface currents for floatables, bacteria, spill response
Theme 4. Coastal Flooding | Weather forecast ensemble validation | Assimilation dataset for forecast models |  | SSTs assimilation into forecast models | Assimilation dataset for forecast models | Nested forecast ensembles
Theme 5. Offshore Energy | Historical analysis & wind model validation | Historical current analysis & wind model validation |  | Historical analysis surface fronts & plumes for siting | Historical analysis of subsurface fronts & plumes | Coupled ocean-atmosphere models for resource estimates
Integration Matrix: Capabilities Support Multiple Themes
MARACOOS Integration Matrix

## Slide 5
Regional Priority Themes | Regional Observation & Modeling Capabilities |  |  |  |  | 
 | Weather Mesonet | HF Radar Network | Statistical STPS | Satellite Imagery | Glider Surveys | Dynamical Ocean Forecasts
Theme 1. Maritime Commerce & Safety | Operational Input to USCG SAROPS | Operational input to USCG SAROPS | Operational input to USCG SAROPS | SST for survivability planning | Assimilation dataset for forecast models | Surface currents for SAROPS
Theme 2. Fisheries | Weather forecast ensemble validation | Circulation and divergence maps for habitat |  | SST & Color for habitat | Subsurface T & S for habitat | 3-D fields of T, S, circulation for habitat
Theme 3. Public Health & Water Quality | Winds for transport, river plumes, & upwelling | Surface currents for floatables, bacteria, spill response | Surface currents for floatables, bacteria, spill response | Ocean color for river plumes | Nearshore dissolved oxygen surveys | Surface currents for floatables, bacteria, spill response
Theme 4. Coastal Flooding | Weather forecast ensemble validation | Assimilation dataset for forecast models |  | SSTs assimilation into forecast models | Assimilation dataset for forecast models | Nested forecast ensembles
Theme 5. Offshore Energy | Historical analysis & wind model validation | Historical current analysis & wind model validation |  | Historical analysis surface fronts & plumes for siting | Historical analysis of subsurface fronts & plumes | Coupled ocean-atmosphere models for resource estimates
Integration Matrix: Capabilities Support Multiple Themes
MARACOOS Integration Matrix
+ Long-term Scientific Archive

## Slide 6
 | Bays, Rivers, Near Shore (< 3 NM) | Offshore (> 3 NM to 200 NM) | Total
Cases | 2,433 | 247 | 2,688
Lives Saved | 500 | 96 | 596
Lives Assisted | 3,332 | 319 | 3,651
Lives Lost | 160 | 14 | 174
Search And Rescue Cases
in MARACOOS Region
U.S. Coast Guard Search And Rescue Data, FY2014

## Slide 7: Surface Current Mapping Capability
25 MHz
Radar l: 12 m Ocean l: 6 m
Range: >30 km Resolution: 1 km
13 MHz
Radar l: 23 m Ocean l: 12 m
Range: >80 km Resolution: 3 km
05 MHz
Radar l: 60m Ocean l: 30 m
Range: >180 km Resolution: 6 km

## Slide 8
Mid-Atlantic Bight HF Radar Network
Mid-Atlantic HF Radar Network
17 Long-Range CODARs
8 Medium-Range CODARs
16 Short-Range CODARs
41 Total CODARs in Region
+5 CODARs Roaming
46 Total CODARs
Triple Nested, Multi-static, Multi-use
Industry Partner: CODAR Ocean Sensors
1000 km
Cape to Cape

## Slide 9
HFR Data Quality Assurance/Quality Control (QA/QC)
Plotting QC flags in real time
From
QARTOD
Manual for
HF Radar
Regional Information Coordination Entity -
RICE

## Slide 10: HF Radar Data Real Time Flow Chart
Level 0
Nov. 2017
Data levels defined by NASA Earth Science Reference Handbook ( 2006, p.31)
Level 1
Level 2
Level 3
Level 4
Green – Operational
Yellow – Development
Red - Planned
Quality Assurance
Manufacturer recommended Antenna Patterns not older than 1 year
Weekly 11-point remote site inspections
Physical site inspection every 6 months
QARTOD
R Test 1: SNR Ratio, Filter < 7dB
S Test 2: Cross Spectra Covariance Matrix Eigenvalue
S Test 3: Direction of Arrival Magnitude
S Test 4: Direction of Arrival Signal Width
S Test 5: Positive Definiteness 2x2 Signal Matrix
R Test 6: Syntax, Filter
R Test 7: Max Threshold, Filter > 150 cm/s (13/25 MHz) 300 cm/s (5 MHz)
R Test 8: Radial Valid Location, Filter
D Test 9: Radial Count, Filter < 300
S Test 10: Spatial Median Test
S Test 11: Temporal Gradient
S Test 12: Average Radial Bearing
S Test 13: Synthetic Radial
R Test 14: Data Density Threshold, Filter, At least 3 vectors from 2 separate stations
R Test 15: GDOP, OI Uncertainty, Flag > 0.6 in U or V Velocity
R Test 16: Max. Speed Threshold , Filter > 150 cm/s (13/25 MHz) 300 cm/s (5 MHz)
S Test 17: Spatial Median Test
Requires SeaSonde Radial Metric Processing
R Required
SR Strongly Recommended
S Suggested
D Development
For IOOS HFR DAC

## Slide 11: Automated Radial Diagnostic
Displays Most Recent Radial File
Displays Preferred Radial Type for Total Processing
If radial file older than 12 hours
If radial count drops below 200

## Slide 12: Radial Web Server
Rutgers COOLroom CODAR Wall
Human in the Loop QA/QC

## Slide 13: HF Radar Data Delayed Mode Flow Chart
Level 0
Nov. 2017
Data levels defined by NASA Earth Science Reference Handbook ( 2006, p.31)
Plot hardware diagnostic data to identify questionable time periods.
Plot radial diagnostic data to identify questionable time periods.
Determine what stations need to be reprocessed for specific time periods
Generate reprocessing time line with appropriate file type (ideal or measured) and antenna patterns.
Generate archived best radial data set.
Create totals from best radial data set.
Level 1
Level 2
Level 3
Level 4
Green – Operational
Yellow – Development
Red - Planned
For NCEI Archive

## Slide 14: Generate Surface Current Maps Every Hour for a Decade
5 MHz- 17 Stations
13 MHz- 7 Stations
25 MHz- 16 Stations
Outside- 6 Stations
TOTAL – 46 Stations
Winter Storm Jonas
2016/01/23 20:00 UTC
Delayed Mode
Decadal Mean Currents
for Scientific Analysis
Real-time
Hourly Maps for
Search And Rescue

## Slide 15
Grid Points for USCG 80-80 Metric
U.S. Coast Guard
HF Radar Metrics
Data quality: Produce better results than existing products (Proven in the USCG tests)
2) Data availability:
Total Current Vectors:
80% Spatial Coverage
80% of the Time
USCG SAR Grid
National HFR Grid

## Slide 16: Search And Rescue Data Availability Metrics
MARACOOS 17-Site Long Range Network:
Consistently exceeds U.S. Coast Guard 80-80 Metric
80 % spatial coverage 80% of the time
Achieved through site resiliency and active spares approach.
Accomplished with 2.5 Field Technicians
Every
6 Months since 2011

## Slide 17: Resilient CODAR Shore Site: Phase 1 Shed, Enclosure, Tx/Rx, Comms, Power, GPS, AIS
Enclosure
Shed
monitor
A.C. unit
transmitter
computer & external hard drive
UPS system
receiver
Two lines of Communication
Lightning Protection

## Slide 18: Resilient CODAR Shore Site: Phase 2
BEFORE
AFTER
Raised Platforms
Shed Lightning Protection
Uninterruptible Power Supplies
Antenna Bases 6’ Deep
Radar Lightning Protection

## Slide 19
Bottom temperature
Data used [… real-time SOURCE] *THREDDS Data Server
72-hour forecast NAM 0Z cycle at 2 am EST [NCEP NOMADS]
RU regional CODAR hourly [RU TDS*]
RU glider T,S [RU TDS]
USGS daily average flow available 11:00 EST [USGS waterdata]
AVHRR IR passes 6-8 per day [MARACOOS TDS]
REMSS MW-IR blended SST daily average [NASA PO-DAAC]
HYCOM NCODA 7-day forecast updated daily [NRL]
Jason-2, CryoSat, AltiKa along-track altimeter OGDR [RADS.nl]
SOOP XBT/CTD, Argo floats, on GTS [NOAA OSMC ERDDAP]
Rutgers ROMS 4DVAR uses all available data from a modern coastal ocean observing system
  more and diverse data is better (T, S, u, sea level)
  bias correction to OBC and MDT is essential
Useful subsurface skill for real-time applications:
  4 days for temperature and salinity;
  1-2 days for velocity
Future directions: variational methods for observing system design; coupling; ecosystems
4-day forecast
2-day forecast
Data assimilation analysis/hindcast
Forward model after bias removal
Forward model
depth
correlation

## Slide 20
Transition Objective –
Operational Use of HF Radar Surface Currents for Search And Rescue
Surface Currents
Search And Rescue Optimal Planning System (SAROPS)
Data Acquisition
Data Product Generation & Management

## Slide 21: USCG Evaluation Process - 5000 Virtual Drifters & 1 Real Drifter: Compare Search Areas after X Hours
HYCOM @ 96 Hours
Search Area = 36,000 km2
CODAR @ 96 Hours
Search Area = 12,000 km2
232 km
154 km
123 km
100 km
Notes: HYCOM (Low Conf) 48 hours

## Slide 22
May 4, 2009: After a year of USCG testing, NOAA announces on
U.S. Department of Commerce Website that
MARACOOS CODAR is Operational in USCG SAROPS
2009-2010 Activity:
Bring all
sustained regional-scale HFR networks up to operational status in USCG SAROPS
3 West Coast Regions for
California & Oregon are ready.

## Slide 23: 2011-2014 2016-2017
USCG SAROPS Ocean Current Product Requests
Global HYCOM Products – Always there “100-100” metric
HF Radar Data & Statistical Predictions – #8
Assimilative Regional Espresso ROMS - not on the list
Global HYCOM Products – Still Always there “100-100” metric
HF Radar Data & Statistical Predictions – up to #6
Assimilative Regional Espresso ROMS - up to #4

## Slide 24
HFR Data
Navy HYCOM Region 1
2016 Surface Current Drifter Skill Score
National Search and Rescue School
Yorktown, VA
January 19, 2017
Coast Guard Sector NY
Staten Island, NY
March 21, 2017
Active Education & Outreach to USCG Users of the HFR Data & Data Assimilative Products
No HFR Assimilation

## Slide 25: Coast Guard Wind & Current Data Requests
Requests June 1 to December 1, 2017

## Slide 26
12 Stations
17

## Slide 27
Decadal Mean
Detided using t_tide
30 hour low pass filter applied
50% temporal coverage per year required
Major Features:
Shelf Slope Front
4 River Outflows
Notes: Like previous studies flow is alongshelf and towards the south
As observed by Steve Lentz The flow speed increases with water depth reaching a maximum at the shelf break
You can also observe this low velocity zone near the bight apex that was first observed by Donglai Gong in his 2010 paper of the surface currents on the NJ shelf

## Slide 28
Inter-Annual Variability
Variability between years averaged over the decade
Tides not included

## Slide 29
Intra-Annual Variability
Variability within a year averaged over the decade
Tides not included

## Slide 30
Average 10-year intra-annual Variability: Winter, Spring, Summer, Autumn
Intra-Annual Variability
Winter
Spring
Summer
Autumn
Notes: Seasonal varibaility of the temperature, break up the
Inter is same varibaility is in the alongshelf
Add river discharge for season in the winter wind plot

## Slide 31
Autumn Mean
September, October and November
River Forcing
Wind Forcing

## Slide 32
Mean Buoy Winds
Fall 2009 Outlier

## Slide 33
Autumn 2009:
Dominant Role of the Wind
Autumn Mean
2009 Flow is Alongshelf

## Slide 34
River Discharge Fall Means – 2011 Outlier

## Slide 35
Autumn Mean
Autumn 2011:
Dominant Role of the Rivers
River Forcing
2011 Flow is Cross-shelf

## Slide 36: Two Decades of Surface Current Measurements Over the Mid Atlantic Continental Shelf
Original installation motivated by Search And Rescue
Additional societal benefits enabled by the real-time data
Highest quality delayed-mode data improves scientific understanding for all

## Slide 37
What can we do together?
Collaborate in the Global HF Radar Network forum http://global-hfradar.org/
Testbed for continuous improvements of upstream operations and advanced capabilities (multi-static, AIS pattern measurements, QC evaluation ….) – sharing new pathways to success
Testbed for demonstrations of new downstream products – sharing our lessons learned on user engagement
Contributing to scientific understanding for the common good – sharing our students.